## Slide 1: FLIGHT MANAGEMENT SYSTEM(FMS)

## Slide 2: INTRODUCTION
A flight management system (FMS) is a fundamental component of a modern airliner's avionics.
An FMS is a specialized computer system that automates a wide variety of in-flight tasks, reducing the workload on the flight crew to the point that modern civilian aircraft no longer carry flight engineers or navigators.
A primary function is in-flight management of the flight plan.
Using various sensors (such as GPS and INS often backed up by radio navigation) to determine the aircraft's position, the FMS can guide the aircraft along the flight plan.

## Slide 3: INTRODUCTION
From the cockpit, the FMS is normally controlled through a Control Display Unit (CDU) which incorporates a small screen and keyboard or touch screen.
The FMS sends the flight plan for display to the Electronic Flight Instrument System (EFIS), Navigation Display (ND), or Multifunction Display (MFD).
The modern FMS was introduced on the Boeing 767, though earlier navigation computers did exist.
Now, systems similar to FMS exist on aircraft as small as the Cessna 182.
In its evolution an FMS has had many different sizes, capabilities and controls. However certain characteristics are common to all FMS.

## Slide 4: INTRODUCTION
All FMS contain a navigation database. The navigation database contains the elements from which the flight plan is constructed.
These are defined via the ARINC 424 standard. The navigation database (NDB) is normally updated every 28 days, in order to ensure that its contents are current.
Each FMS contains only a subset of the ARINC / AIRAC(Aeronautical Information Regulation And Control and steps from the Annex 15 - Aeronautical Information Services (AIS) document and defines a series of common dates and an associated standard aeronautical information ) data, relevant to the capabilities of the FMS.

## Slide 5: COMPONENTS OF FMS
The NDB contains all of the information required for building a flight plan, consisting of:
Waypoints/Intersection
Radio navigation aids including distance measuring equipment (DME), VHF Omni directional range (VOR), non-directional beacons (NDBs) and instrument landing systems (ILSs).
Airports
Runways
Standard instrument departure (SID)
Standard terminal arrival (STAR)
Holding patterns (only as part of IAPs-although can be entered by command of ATC or at pilot's discretion)
Instrument approach procedure (IAP)

## Slide 6: FLIGHT PLAN
The flight plan is generally determined on the ground, before departure either by the pilot for smaller aircraft or a professional dispatcher for airliners.
It is entered into the FMS either by typing it in, selecting it from a saved library of common routes (Company Routes) or via an ACARS data link with the airline dispatch center.
During preflight, other information relevant to managing the flight plan is entered.
This can include performance information such as gross weight, fuel weight and center of gravity.
It will include altitudes including the initial cruise altitude. For aircraft that do not have a GPS, the initial position is also required.

## Slide 7: FLIGHT PLAN
The pilot uses the FMS to modify the flight plan in flight for a variety of reasons.
Significant engineering design minimizes the keystrokes in order to minimize pilot workload in flight and eliminate any confusing information (Hazardously Misleading Information).
The FMS also sends the flight plan information for display on the Navigation Display (ND) of the flight deck instruments Electronic Flight Instrument System (EFIS).
Special flight plans, often for tactical requirements including search patterns, in-flight refueling tanker orbits, calculated air release points (CARP) for accurate parachute jumps are just a few of the special flight plans some FMS can calculate.

## Slide 8: POSITION DETERMINATION
Once in flight, a principal task of the FMS is to determine the aircraft's position and the accuracy of that position. Simple FMS use a single sensor, generally GPS in order to determine position.
But modern FMS use as many sensors as they can, such as VORs, in order to determine and validate their exact position.
Some FMS use a Kalman filter to integrate the positions from the various sensors into a single position. Common sensors include:
Airline quality GPS receivers act as the primary sensor as they have the highest accuracy and integrity.

## Slide 9: POSITION DETERMINATION
Radio aids designed for aircraft navigation act as the second highest quality sensors. These include :
Scanning DME (distance measuring equipment) that check the distances from five different DME stations simultaneously in order to determine one position every 10 seconds.
VORs (VHF Omni directional radio range) that supply a bearing. With two VOR stations the aircraft position can be determined, but the accuracy is limited.
Inertial reference systems (IRS) use ring laser gyros and accelerometers in order to calculate the aircraft position. They are highly accurate and independent of outside sources. Airliners use the weighted average of three independent IRS to determine the “triple mixed IRS” position.

## Slide 10: POSITION DETERMINATION
The FMS constantly crosschecks the various sensors and determines a single aircraft position and accuracy.
The accuracy is described as the Actual Navigation Performance (ANP) a circle that the aircraft can be anywhere within measured as the diameter in nautical miles.
Modern airspace has a set required navigation performance (RNP). The aircraft must have its ANP less than its RNP in order to operate in certain high-level airspace.

## Slide 11: GUIDENCE
Given the flight plan and the aircraft's position, the FMS calculates the course to follow.
The pilot can follow this course manually (much like following a VOR radial), or the autopilot can be set to follow the course.
The FMS mode is normally called LNAV or Lateral Navigation for the lateral flight plan and VNAV or vertical navigation for the vertical flight plan.
VNAV provides speed and pitch or altitude targets and LNAV provides roll steering command to the autopilot.