## Slide 1: INERTIAL REFRENCE SYSTEM

## Slide 2: INTRODUCTION
The inertial reference system (IRS) provides inertial navigation data to user systems.
It uses a ring laser gyro instead of the conventional rate gyro to sense angular rate about the roll, pitch and yaw axes.
The system is termed strap down since its sensors are, in effect, directly mounted to the airframe.
The inertial reference system (IRS) includes two inertial reference units (IRU), one inertial system display unit (ISDU), one mode select unit (MSU), one master caution unit (MCU), two digital/analog adapters (DAA) and two radio digital distance magnetic indicators (RDDMI).
The IRS provides the inertial navigation data and the inertial flight control data to other systems.

## Slide 3: INTRODUCTION
The main function of each IRU is to sense and compute linear accelerations and angular turning rates about the airplane's pitch, roll, and yaw axes.
This data is used for pitch and roll displays and navigational computations.
Each IRU contains three laser gyros and three accelerometers. These sense angular rates and linear accelerations, respectively.
The sensed data is resolved to local vertical coordinates and combined with air data inputs to compute the following:

## Slide 4: INTRODUCTION
(1) Position (latitude, longitude)
(2) Attitude (pitch, roll, yaw)
(3) True and magnetic heading
(4) Wind speed and direction
(5) Velocity
(6) Accelerations
(7) Angular rate data
(8) Altitude

## Slide 5: INTRODUCTION
The IRS outputs are displayed on the flight instrument system displays.
They are also displayed on the flight management computer system control display unit (FMCS-CDU)
Preselected parameters are also displayed on the inertial system display unit (ISDU).

## Slide 6: IRS Theory of Operation
A. General
The IRS provides basic heading and attitude reference accomplished through computations based on accelerometer and laser gyro sensed signals.
Three accelerometers and three laser gyros are used. The accelerometers and laser gyros are of the strap-down type and are positioned in the inertial reference units so that they are oriented along each of the three axis of the airplane.
This orientation allows the IRU to sense accelerations along and rotation about each of the three axis.

## Slide 7: IRS Theory of Operation
Computer manipulation of the signals from all six sensors provide the basic heading and attitude reference signals along with present position, accelerations, ground speed, drift angle and attitude rate information.
The first requirement which must be met for proper IRS operation is alignment.
IRS alignment basically consists of determination of local vertical and initial heading.

## Slide 8: IRS Theory of Operation
B. Alignment
IRS alignment consists of determining local vertical and initial heading.
Both accelerometer and laser gyro inputs are used for alignment.
The alignment computations use the basic premise that the only accelerations during alignment are due to the earth's gravity; the only motion during alignment is due to the earth's rotation.
Accelerations due to gravity are always perpendicular to the earth's surface and thus define the local vertical.

## Slide 9: IRS Theory of Operation
This local vertical is used to fix the attitude data so that it is accurately referenced to vertical.
Initially, only a coarse vertical is established. Once vertical is established, the laser gyro sensed earth rate components are used to establish the heading of the airplane.
As the alignment continues, both the vertical reference and the heading determinations are fine tuned for maximum accuracy.