## Slide 1: FIBER OPTICS

## Slide 2: ADVANTAGES AND DISADVANTAGES
Optical fibers offer some very significant advantages over conventional copper cables. These include:
• optical fibers are lightweight and of small physical size;
• exceptionally wide bandwidth and very high data rates can be supported;
• relative freedom from electromagnetic interference;
• significantly reduced noise and cross-talk compared with conventional copper cables;
• relatively low values of attenuation within the medium;
• high reliability coupled with long operational life;
• electrical isolation and freedom from earth/ ground loops.

## Slide 3: ADVANTAGES AND DISADVANTAGES
The reduction in weight that results from the use of fibre optical cabling can yield significant fuel savings. Copper cabling is typically five times heavier than polymer optical fibre cabling and 15 times heavier than silica optical fibre. On a large, latest-generation aircraft with sophisticated avionics, the total saving in weight can be as much as 1,300 kg.
There are very few disadvantages of optical fibres. They include:
• industry resistance to the introduction of new technology;
• need for a high degree of precision when fitting cables and connectors;
• concerns about the mechanical strength of fibres and the need to ensure that cable bends have a sufficiently large radius to minimize losses and the possibility of damage to fibres.

## Slide 4: PROPAGATION IN OPTICAL FIBRES
Essentially, an optical fibre consists of a cylindrical silica glass core surrounded by further glass cladding.
The fibre acts as a channel (or waveguide) along which an electromagnetic wave can pass with very little loss.
Fibre-optics are governed by the fundamental laws of reflection and refraction. For example, when a light wave passes from a medium of higher refractive index to one of lower refractive index, the wave is bent towards the normal, as shown in Figure 10.1a.
Conversely, when travelling from a medium of lower refractive index to one of higher refractive index, the wave will be bent away from the normal, as shown in Figure 10.1b.
In this latter case, some of the incident light will be reflected at the boundary of the two media and, as the angle of incidence is increased, the angle of refraction will also be increased until, at a critical value, the light wave will be totally reflected (i.e. the refracted ray will no longer exist, as shown in Figure 10.2).

## Slide 5: PROPAGATION IN OPTICAL FIBRES
The angle of incidence at which this occurs is known as the critical angle, .
The value of depends on the absolute refractive indices of the media and is given by:
=
where n1 and n2 are the refractive indices of the more dense and less dense media, respectively.

## Slide 8: PROPAGATION IN OPTICAL FIBRES
Optical fibres are manufactured by drawing silica glass from the molten state and they are thus of cylindrical construction.
The more dense medium (the core) is surrounded by the less dense medium (the cladding).
Provided the angle of incidence of the input wave is larger than the critical angle, the light wave will propagate inside the core by means of a series of total internal reflections.
Any other light waves that are incident on the upper boundary at an angle > will also propagate along the inner medium.
Conversely, any light wave that is incident upon the upper boundary with will pass into the outer medium and there be lost by scattering and/or absorption.

## Slide 9: LAUNCHING
The cone of acceptance (see Figure) is the complete set of angles which will be subject to total internal reflection.
Rays entering from the edges will take a longer path through the fibre but will travel faster because of the lower refractive index of the outer layer.
The numerical aperture determines the bandwidth of the fibre and is given by:
Numerical aperture, A = sin
Clearly, when a number of light waves enter the system with differing angles of incidence, a number of waves (or modes) are able to propagate.
This multimode propagation is relatively simple to achieve but has the attendant disadvantage that, since the light waves will take different times to pass through the fibre, the variation of transit time will result in dispersion, which imposes an obvious restriction on the maximum bit-rate the system will support.

## Slide 11: LAUNCHING
There are two methods for reducing multimode propagation.
One uses a fibre of graded refractive index, while the other uses a special single mode (or monomode) fibre.
The inner core of this type of fibre is reduced in diameter so it has the same order of magnitude as the wavelength of the incident wave.
This ensures that only one mode will successfully propagate.

## Slide 13: Attenuation
The loss within an optical fibre arises from a number of causes, including: absorption, scattering in the core (due to non-homogeneity of the refractive index), scattering at the core/cladding boundary, and losses due to radiation at bends in the fibre.
Note that the attenuation coefficient of an optical fibre (see Figure) refers only to losses in the fibre itself and neglects coupling and bending losses (which can be significant).
In general, the attenuation of a good quality fibre can be expected to be less than 2 dB per kilometer at a wavelength of 1.3 μm (infrared).
Hence a 50 m length of fibre can be expected to exhibit a loss of around 0.1 dB.

## Slide 15: Attenuation
Whereas the attenuation coefficient of an optical fibre is largely dependent upon the quality and consistency of the glass used for the core and cladding, the attenuation of all optical fibres varies widely with wavelength.
The typical attenuation/wavelength characteristic for a monomode fibre is shown in Figure. It should be noted that the sharp peak at about 1.39 μm arises from excess absorption within the monomode fibre.
Monomode fibres are now a common feature of ground-based high-speed data communication systems and manufacturing techniques have been developed that ensure consistent and reliable products with low attenuation and wide operational bandwidths.
However, since monomode fibres are significantly smaller in diameter than their multimode predecessors (see Figure), a consistent and reliable means of cutting, surface preparation, alignment and interconnection is essential, and for this reason slower multimode fibres are still prevalent in current aircraft designs.

## Slide 16: DISPERSION AND BANDWIDTH
A simple one-way (simplex) fibre-optic data link is shown in Figure .
The optical transmitter consists of an infrared light emitting diode (LED) or low power semiconductor laser diode coupled directly to the optical fibre.
The diode is supplied with pulses of current from a bus interface.
These pulses of current produce equivalent pulses of light that travel along the fibre until they reach the optical receiver unit.
The optical receiver unit consists of a photodiode or phototransistor that passes a relatively large current when illuminated and negligible current when not.
The pulses of current at the transmitting end are thus replicated at the receiving end.
The maximum data rate (and consequently the bandwidth) of the optical data link depends on the ability of the system shown in Figure to faithfully reproduce a train of narrow digital pulses.

## Slide 18: DISPERSION AND BANDWIDTH
Unfortunately, in a multimode fibre different modes travel at different velocities, as shown earlier in Figure 10.2d.
This phenomenon is known as dispersion and it has the effect of stretching the output pulse, as shown in Figure .
When digital data is supplied to the optical transmitter, the stretching of pulses imposes an upper limit on the rate at which the pulses can be transmitted.
In other words, the data rate is determined by the amount of dispersion simply because a longer bit interval means fewer bits can be transmitted in the same unit of time (see Figure).

## Slide 20: PRACTICAL OPTICAL NETWORKS
The Boeing 777 was the first commercial aircraft to enter production with an optical fibre-based LAN for onboard data communications.
The system was originally developed in the 1980s and it comprised an avionics local area network (AVLAN) fitted in the flight deck and electrical equipment bay, together with a cabin local area network (CABLAN) fitted in the roof of the passenger cabin.
These two fibre-optic networks conform to the ARINC 636 standard, which was adapted for avionics from the fibre distributed interface (FDDI) in order to provide a network capable of supporting data rates of up to 100 Mbps.

## Slide 21: Fibre-optic cable construction
The construction of a typical fibre-optic cable is shown in Figure .This comprises:
• five optical fibres and two filler strands;
• separator tape;
• aramid yarn strength member;
• an outer jacket.
The cable has an overall diameter of about 0.2 inches and the individual optical fibre strands have a diameter of 140 μm (approximately 0.0055 inches).
A protective buffer covers each fibre and protects it during manufacture, and increases mechanical strength and diameter in order to make handling and assembly easier.
The buffers are coded in order to identify the fibres using colours (blue, red, green, yellow and white).
The filler strands are made from polyester and are approximately 0.035 inches in diameter.

## Slide 22: Fibre-optic cable construction
A polyester separator tape covers the group of five fibres and two filler strands.
This tape is manufactured from low friction polyester and it serves to make the cable more flexible.
A layer of woven aramid (or Kevlar) yarn provides added mechanical strength and protection for the cable assembly.
The outer thermoplastic jacket (usually purple in color) is fitted to prevent moisture ingress and also to provide insulation.

## Slide 24: Fibre-optic connectors
The essential requirements for connectors used with optical fibres are that they should be:
• reliable
• robust
• precise and repeatable (even after numerous mating operations)
• suitable for installation without specialist tooling
• low loss
• low cost.

## Slide 25: Fibre-optic connectors
While the loss exhibited by a connector may be quoted in absolute terms, it is often specified in terms of an equivalent length of optical fibre.
If, for example, six connectors are used on a cable run and each connector has a loss of 0.5 dB, the total connector loss will be 3 dB.
This is equivalent to several kilometers of low-loss fibre! A typical fibre-optic cable connector arrangement is shown in Figure .This comprises:
• alignment keys and grooves
• guide pins and cavities
• colored alignment bands
• three start threads.

## Slide 27: Fibre-optic connectors
Each connector has alignment keys on the plug and matching alignment grooves on the receptacle.
These are used to accurately align the connector optical components; the guide pins in the plug fit into cavities in the receptacle when the plug and receptacle connect.
In order to ensure that the connector is not over-tightened (which may cause damage to the fibres) the pins of the plug are designed to provide a buffer stop against the bottom of the cavities in the receptacle.
The plug and receptacle have ceramic contacts that are designed to make physical contact when properly connected (the light signal passes through the holes in the end of the ceramic contacts when they are in direct physical contact with each other).

## Slide 28: Fibre-optic connectors
The coupling nut on the plug barrel has a yellow band, while the receptacle barrel has a red and a yellow band.
A correct connection is made when the red band on the receptacle is at least 50 per cent covered by the coupling nut.
This position indicates an effective connection in which the optical fibres in the plug are aligned end-to-end with the fibre in the receptacle.
Three start threads on the plug and receptacle ensure a straight start when they join.
The recessed receptacle components prevent damage from the plug if it strikes the receptacle at an angle.
The plug and receptacle are automatically sealed in order to prevent the ingress of moisture and dust.

## Slide 29: OPTICAL NETWORK COMPONENTS
Several other components are found in optical fibre networks.
These include couplers (with three or four ports), switches (using mirrors to deflect beams into different fibre strands) and routers.
These last named devices are designed to control the routing of signals through the LAN and they comprise switches, processors, controllers and one or more bus interfaces.
The router processor sends control signals to the bypass switch unit (BSU).Typical BSU control signals are:
• PRI HI
• PRI RTN
• SEC HI
• SEC RTN.

## Slide 30: OPTICAL NETWORK COMPONENTS
A logic high on PRI HI or SEC HI connects the BSU to the fibre-optic ring. A logic low on PRI HI or SEC HI disconnects the BSU from the fibre optic ring.
The PRI RTN and SEC RTN control signals are grounds (active-low inputs) to the BSU switch relays.
The fibre optic interface changes BSU fibre-optic signals to electronic signals and electronic signals to BSU fibre optic signals.