## Slide 1
Fluid : fluid is a substance that continually deforms (flows) under an applied shear stress, or external force. Fluids are a phase of matter and include liquids, gases and plasmas. They are substances which cannot resist any shear force applied to them.

## Slide 2: Types of Fluid
Ideal Fluid
Real Fluid
Newtonian Fluid
Non-Newtonian Fluid
Ideal plastic fluid
Incompressible fluid
Compressible fluid

## Slide 4
Ideal fluid
A fluid, which is incompressible and having no viscosity, is known as an ideal fluid. Ideal fluid is only an imaginary fluid as all the fluids, which exist, have some viscosity.

## Slide 5
Real fluid
A fluid, which possesses viscosity, is known as real fluid. All the fluids, in actual practice, are real fluids.

## Slide 6
Newtonian fluid
A real fluid, in which shear stress in directly proportional to the rate of shear strain or velocity gradient, is known as a Newtonian fluid.
Example : Water, Benzine etc

## Slide 7
Non Newtonian fluid
A real fluid, in which shear stress in not directly proportional to the rate of shear strain or velocity gradient, is known as a Non Newtonian fluid.
Example : Plaster, Slurries, Pastes etc

## Slide 8
Ideal plastic fluid:
A fluid, in which shear stress is more than the yield value and shear stress is proportional to the rate of shear strain or velocity gradient, is known as ideal plastic fluid.

## Slide 9
Incompressible fluid
A fluid, in which the density of fluid does not change which change in external force or pressure, is known as incompressible fluid. All liquid are considered in this category.

## Slide 10
Compressible fluid:
A fluid, in which the density of fluid changes while change in external force or pressure, is known as compressible fluid. All gases are considered in this category.

## Slide 11: Tabular representation of fluid types
Types of fluid | Density | Viscosity
Ideal fluid | Constant | Zero
Real fluid | Variable | Non zero
Newtonian fluid | Constant/ Variable | T = u(du/dy)
Non Newtonian fluid | Constant/ Variable | T ≠ u(du/dy)
Incompressible fluid | Constant | Non zero/zero
Compressible fluid | Variable | Non zero/zero

## Slide 12
Types Of Fluid Flow:-
Steady & Unsteady Flows.
Uniform & Non-uniform Flows.
Laminar & Turbulent Flows.
Compressible & Incompressible Flows.
Rotational & Irrotational Flows.
One , Two & Three Dimensional Flows.

## Slide 13
Steady & Unsteady Flows:-
Steady Flows:-
In which the fluid Characteristics Like velocity, pressure, density , etc. At a Point do not change with time.

## Slide 14
Unsteady Flow:-
In which the fluid velocity , pressure or density at a point changes with respect to time.

## Slide 15: Flow :-
Uniform & Non-uniform
Uniform Flow:-
In which the velocity at given time does not change with respect to space ( length of direction of the flow ).

## Slide 16
Non-Uniform Flow:-
In which the velocity at any time changes with respect to space.
Changing in space

## Slide 17
Laminar & Turbulent
flows:-
Laminar Flow:-
 in which the fluid particles move along well defined paths or stream line.
Fig. Laminar Flow

## Slide 18
Turbulent Flow:-
fluid moves in very irregular paths or zig – zag Way.
velocity at a point fluctuates.

## Slide 19: Compressible & Incompressible Flows:-
Compressible Flows:-
In which the density of the fluid changes from point to point.
The density is not constant for the fluid.
Incompressible Flows:-
In which the density of fluid changes from point to point.
the density is constant for the fluid.

## Slide 20: Rotational & Irrotational Flows:-
Rotational Flow :-
In which the fluid particles while flowing along stream lines, Also rotate about their own axis.
Irrotational Flow:-
In which the fluid particles while flowing along stream lines, do not rotate about their own axis.

## Slide 21: One Dimensional Flow:-
One , Two & Three Dimensional Flows:-
In which the flow parameter such as velocity is a function of time and
one space co-ordinate only.

## Slide 22: Two Dimensional Flow:-
In which the velocity is a function of time and
two rectangular space co-ordinates.

## Slide 23: Three Dimensional Flow:-
In which the velocity is the function of time and
Three mutually perpendicular directions.

## Slide 24: Reynolds number
Reynolds number is a dimensionless value which is applied in fluid mechanics to represent whether the fluid flow in a duct is steady or turbulent. This value is obtained by comparing the inertial force with the viscous force.
The Reynolds number id denoted by Re.
Reynolds number is given by,
Reynolds Number = Inertial Force / Viscous Force
The Reynolds number formula is expressed by,

## Slide 25
For a laminar flow, the Reynolds number is less than 2100.
Turbulent flow the Reynolds number is greater than 4000.
In the transition flow the Reynolds number ranges from 2100 to 4000.

## Slide 26
The velocity profile in turbulent flow is much fuller than that in laminar flow, with a sharp drop near the surface.
The turbulent boundary layer can be considered to consist of four regions:
  Viscous sublayer
  Buffer layer
  Overlap layer
  Turbulent layer
The intense mixing in turbulent flow enhances heat and momentum transfer, which increases the friction force on the surface and the convection heat transfer rate.