## Slide 1
“Principle of Mineral Processing”
Subject Code : MT 410302

## Slide 2
Unit 1
Introduction and scope of mineral processing in extractive metallurgy,
Mineral resources in India, Physical characteristics exploited in mineral
processing, Terminology in mineral processing
Physical and chemical characteristics of industrial minerals such as
Haematite, Magnetite, Galena, Chalcopyrite, Azurite, Monazite, Cassiterite, Chromite, Bauxite and Ilmenite; Economics of ore processing. Selectivity index.
Principle of Mineral Processing - Syllabus

## Slide 3
Mineral – Naturally occuring chemical compound having definite chemical composition & crystal structure.
Ore – Natural aggregation of minerals from which a metal or metallic compound can be recovered.
Mineral Processing of raw minerals :
Marketable products without destroying physical & chemical identity of minerals
Introduction
Chalcopyrite
Galena ( PbS)

## Slide 4
4

## Slide 5
5
Introduction
Ore Deposit
An occurrence of minerals or metals in sufficiently high concentration to be profitable to mine and process using current technology and under current economic conditions.
Ore Grade
Ore grade is the concentration of economic mineral or metal in an ore deposit.
Weight percentage (base metals) Grams/tonne
or oz/ton (precious metals)

## Slide 6
6
Introduction

## Slide 7
7
Economically Important Metals Typical Grades of Ore Deposits

## Slide 8
Economic & Technical justification of ore dressing
- Less expensive than hydro & pyro process
- savings in freight
- reduced metal losses in slag
- lower smelting cost
Scope of mineral dressing process - elimination of
a) unwanted chemical species/gangue
b) unsuitable particle size
Most minerals - Crystalline in nature with crystal structure
Introduction

## Slide 9
Native Form :
Cu, Gold , Silver, Bismuth, Diamond
Sulphides
Chalcopyrite CuFeS2, Galena PbS , Sphalerite ZnS
Oxides & Hydroxides :
Cuprite Cu2O , Rutile TiO2, Hematite Fe2O3
Carbonates :
Calcite CaCO3 , Magnesite MgCO3, Cerussite PbCO3
Types of minerals

## Slide 10
Halides :
Salt NaCl , Fluorite CaF2, Cryolite Na3AlF6
Nitrates :
Soda Nitre NaNO3 , Nitre KNO3
Sulphates :
Barytes BaSO4 , Anglesite PbSO4, Gypsum CaSO4.2H2O
Borates :
Borax Na2B4O7.10 H2O
Types of minerals

## Slide 11: Mineral Resources in India

## Slide 12: Mineral Resources in India
Classification of mineral resources in Indian perspective
Surplus Group : Iron ore, barite, bauxite, mica, soapstone, china
clay, gypsum, beach sand, sillimanite, ornamental stone, chromite
(low grade), dolomite and limestone ( cement grade)
Self sufficient Group: Thermal coal, lignite, chromite, pyrite etc.
Satisfactory Group : Zinc, magnesite, fireclay, ilmenite sand ( titanium) rutile, sand (titanium)

## Slide 13
Properties used for Separation

## Slide 14: Physical Properties of Minerals

## Slide 15
Stages involved in Ore processing

## Slide 16
Ratio of concentration
Wt of conc / wt of Feed
Recovery
Assay value in Conc. / assay value in feed
Selectivity Index
Geometrical mean of recoveries & rejections
S.I. = ( CPb/TPb*Tg/Cg)½
Pb-value in conc. - 60.5% & Tailing - 0.2% ,
Gangue in conc - 12.6% , & Tailing - 94.6%
SI = ((60.5/0.2)*(94.6/12.6)) ^1/2 =47.6
Quantitative Measurement

## Slide 17
Economic Recovery or Efficiency
% ratio of actual value of concentrate per ton of ore to
the theoretical value of concentrate
Example :
130 kg of Pb concentrate / T of ore worth Rs 16000
Theoretically 120 kg pure Galena worth Rs 18000.
Actual recovery = (0.13*16000)/(0.12*18000) =96.3% ,
Quantitative Measurement

## Slide 18
18
Metal Accounting
Uses
  steady-state accounting of mass flows in a system
  evaluation of metallurgical testwork
  comparison of two different mills or circuits
  process control of an operation plant
Properties of the Balance
  requires samples for assay and weights/flowrates
accuracy of the assays used
  turnaround time of assays

## Slide 19
19
Metallurgical Balances
The method relies on equations and tables
Equations
2-Product Formula
F = C + T
Ff = Cc + Tt
where F = feed tonnage rate or 100%
C = concentrate tonnage or weight%
T = tailing tonnage or weight%
and f, c, t = assay of each respective stream (%, g/t, ppm, etc.)
F
C
T

## Slide 20
20
Metallurgical Balances
C = 100 * (f-t)/(c-t)
%Recovery = 100 * c(f-t) /f(c-t)
2-Product Formula Solution
The Metallurgical Balance Table
Weight%
Assay (%)
Units
%Recovery
Product
Concentrate
Tailing
Feed
T
100
C
c
t
f
Tt
100f
100
Cc
Cc/f
Tt/f