## Slide 1: INSTRUCTION SET OF 8085

## Slide 2: Instruction Set of 8085
An instruction is a binary pattern designed inside a microprocessor to perform a specific function.
The entire group of instructions that a microprocessor supports is called Instruction Set.
8085 has 246 instructions.
Each instruction is represented by an 8-bit binary value.
These 8-bits of binary value is called Op-Code or
Instruction Byte.

## Slide 3: Classification of Instruction Set
Data Transfer Instruction
Arithmetic Instructions
Logical Instructions
Branching Instructions
Control Instructions

## Slide 4: 1.Data Transfer Instructions
These instructions move data between registers, or between memory and registers.
These instructions copy data from source to destination(without changing the original data ).

## Slide 5: MOV-Copy from source to destination
Opcode Operand
MOV
Rd, Rs M, Rs Rd, M
This instruction copies the contents of the source register into the destination register. (contents of the source register are not altered)
If one of the operands is a memory location, its location is specified by the contents of the HL registers.
Example: MOV B, C or MOV B, M

## Slide 6
A 20 B
20
A |  | F | 
B | 30 | C | 
D |  | E | 
H | 20 | L | 50
A | 20 | B | 
BEFORE EXECUTION
AFTER EXECUTION
MOV B,A
A |  | F | 
B | 30 | C | 
D |  | E | 
H | 20 | L | 50
A F |  |  | 
B |  | C | 
D |  | E | 
H | 20 | L | 50
A F |  |  | 
B |  | C | 40
D |  | E | 
H | 20 | L | 50
MOV M,B
MOV C,M
40
40
30

## Slide 7: MVI-Move immediate 8-bit
Opcode Operand
MVI
Rd, Data M, Data
The 8-bit data is stored in the destination register or memory.
If the operand is a memory location, its location is specified by the contents of the H-L registers.
Example: MVI B, 60H or MVI M, 40H

## Slide 8: BEFORE EXECUTION
A F |  | 
B |  | C
D E |  | 
H L |  | 
A F |  | 
B | 60 | C
D E |  | 
H L |  | 
AFTER EXECUTION
MVI B,60H
40
HL=2050
2051H
204FH
204F
2051H
MVI M,40H
BEFORE EXECUTION
AFTER EXECUTION
HL=2050

## Slide 9: LDA-Load accumulator
Opcode
Operand
LDA
16-bit address
The contents of a memory location, specified by a 16- bit address in the operand, are copied to the accumulator.
The contents of the source are not altered.
Example: LDA 2000H

## Slide 10
A
30
30
AFTER EXECUTION
A 30
BEFORE EXECUTION
LDA 2000H
2000H
2000H

## Slide 11: LDAX-Load accumulator indirect
Opcode Operand
LDAX
B/D Register Pair
The contents of the designated register pair point to a memory location.
This instruction copies the contents of that memory location into the accumulator.
The contents of either the register pair or the memory location are not altered.
Example: LDAX D

## Slide 12: AFTER EXECUTION
A
F
B
C
D 20 E 30
A
80 F
B
C
D 20 E 30
80
80
BEFORE EXECUTION
LDAX D
2030H
2030H

## Slide 13: LXI-Load register pair immediate
Opcode Operand
LXI
Reg. pair, 16-bit data
This instruction loads 16-bit data in the register pair.
Example: LXI H, 2030 H

## Slide 14
A
F
B
C
H L
A | 80 | F | 
B |  | C | 
H | 90 | L | 30
30
90
50
AFTER EXECUTION
BEFORE EXECUTION
LXI H, 2030
2030H
9030H
2031H
M=50

## Slide 15: LHLD-Load H and L registers direct
Opcode Operand
LHLD
16-bit address
This instruction copies the contents of memory location pointed out by 16-bit address into register L.
It copies the contents of next memory location into register H.
Example: LHLD 2030 H

## Slide 16
A
F
B
C
H L
A |  | F | 
B |  | C | 
H | 85 | L | 00
00
85
60
AFTER EXECUTION
BEFORE EXECUTION
LHLD 2030
2030H
8500H
M=60

## Slide 17: Opcode Operand
STA
16-bit address
The contents of accumulator are copied into the memory location specified by the operand.
Example: STA 2000H
STA-Store accumulator direct

## Slide 18
A
50
50
AFTER EXECUTION
BEFORE EXECUTION
A 50
STA 2000H
2000H
2000H

## Slide 19: STAX-Store accumulator indirect
Opcode Operand
STAX
Reg. pair
The contents of accumulator are copied into the memory location specified by the contents of the register pair.
Example: STAX B

## Slide 20
BEFORE EXECUTION
B 85 C 00
A=1AH
AFTER EXECUTION
STAX B
1A
8500H

## Slide 21: SHLD-Store H and L registers direct
Opcode Operand SHLD 16-bit address
The contents of register L are stored into memory location specified by the 16-bit address.
The contents of register H are stored into the next memory location.
Example: SHLD 2550H

## Slide 22
D E |  |  | 
H | 70 | L | 80
BEFORE EXECUTION
AFTER EXECUTION
SHLD 8500
80
70
8500H
8501H

## Slide 23: XCHG-Exchange H and L with D and E
Opcode Operand
XCHG None
The contents of register H are exchanged with the contents of register D.
The contents of register L are exchanged with the contents of register E.
Example: XCHG

## Slide 24: BEFORE EXECUTION
D | 20 E | 40
H | 70 L | 80
D | 70 | E | 80
H | 20 | L | 40
AFTER EXECUTION
XCHG

## Slide 25: SPHL-Copy H and L registers to the stack pointer
Opcode Operand
SPHL
None
This instruction loads the contents of H-L pair into SP.
Example: SPHL

## Slide 26: BEFORE EXECUTION
SP |  |  | 
H | 25 | L | 00
SPHL
AFTER EXECUTION
SP | 2500
H | 
 | 25 L 00

## Slide 27: XTHL-Exchange H and L with top of stack
Opcode Operand
XTHL None
The contents of L register are exchanged with the location pointed out by the contents of the SP.
The contents of H register are exchanged with the next location (SP + 1).
Example: XTHL

## Slide 28
H
30
L 40
SP
2700
BEFORE EXECUTION
50
60
SP |  | 2700 | 
H | 60 | L | 50
40
30
AFTER EXECUTION
XTHL
2700H
2701H
2702H
2700H
2701H
2702H
L=SP H=(SP+1)

## Slide 29
Opcode | Operand | Description
PCHL | None | Load program counter with H- L contents
The contents of registers H and L are copied into the program counter (PC).
The contents of H are placed as the high-order byte and the contents of L as the low-order byte.
Example: PCHL

## Slide 30: PUSH-Push register pair onto stack
Opcode Operand
PUSH Reg. pair
The contents of register pair are copied onto stack.
SP is decremented and the contents of high-order registers (B, D, H, A) are copied into stack.
SP is again decremented and the contents of low-order registers (C, E, L, Flags) are copied into stack.
Example: PUSH B

## Slide 31: PUSH H

## Slide 32: POP- Pop stack to register pair
Opcode Operand
POP Reg. pair
The contents of top of stack are copied into register pair.
The contents of location pointed out by SP are copied to the low-order register (C, E, L, Flags).
SP is incremented and the contents of location are copied to the high-order register (B, D, H, A).
Example: POP H

## Slide 33: POP H

## Slide 34: IN- Copy data to accumulator from a port with 8-bit address
Opcode Operand
IN
8-bit port address
The contents of I/O port are copied into accumulator.
Example: IN 8C H

## Slide 35: A
10
10
A
10
BEFORE EXECUTION
AFTER EXECUTION
IN 80H
PORT 80H
PORT 80H

## Slide 36: OUT- Copy data from accumulator to a port with 8-bit address
Opcode Operand
OUT
8-bit port address
The contents of accumulator are copied into the I/O port.
Example: OUT 78H

## Slide 37: 10
A 40
40
A 40
BEFORE EXECUTION
AFTER EXECUTION
OUT 50H
PORT 50H
PORT 50H

## Slide 38: 2.Arithmetic Instructions
These instructions perform the operations like:
Addition
Subtract
Increment
Decrement

## Slide 39: Addition
Any 8-bit number, or the contents of register, or the contents of memory location can be added to the contents of accumulator.
The result (sum) is stored in the accumulator.
No two other 8-bit registers can be added directly.
Example: The contents of register B cannot be added directly to the contents of register C.

## Slide 40: ADD
Opcode | Operand | Description
ADD | R M | Add register or memory to accumulator
The contents of register or memory are added to the contents of accumulator.
The result is stored in accumulator.
If the operand is memory location, its address is specified by H-L pair.
Example: ADD B or ADD M

## Slide 41
05
BEFORE EXECUTION
B
C
D
E
H 20 L
50
C
D
50
AFTER EXECUTION
BEFORE EXECUTION
A | 04 |  | 
B | C |  | 05
D | E |  | 
H | L |  | 
AFTER EXECUTION
09
C
D E
H L
ADD C A=A+C
ADD M A=A+M
10
10
2050
2050
A
04
A
B
14
04+05=09
E
H 20 L
04+10=14

## Slide 42: ADC
Opcode | Operand | Description
ADC | R M | Add register or memory to accumulator with carry
The contents of register or memory and Carry Flag (CY) are added to the contents of accumulator.
The result is stored in accumulator.
If the operand is memory location, its address is specified by H-L pair.
All flags are modified to reflect the result of the addition.
Example: ADC B or ADC M

## Slide 43
B
C
05
D
E
H
L
A
50
B
C
20
D
E
H
L
A 56
AFTER EXECUTION
BEFORE EXECUTION
ADC C A=A+C+CY
CY
01
CY
1
A
06
A
37
H
20
L
50
50
ADC M A=A+M+CY
AFTER EXECUTION
BEFORE EXECUTION
30
30
2050H
2050H
H 20 L
06+1+30=37
50+05+01=56

## Slide 44: ADI
Opcode | Operand | Description
ADI | 8-bit data | Add immediate to accumulator
The 8-bit data is added to the contents of accumulator.
The result is stored in accumulator.
All flags are modified to reflect the result of the addition.
Example: ADI 45 H

## Slide 45
A
03
AFTER EXECUTION
BEFORE EXECUTION
ADI 05H A=A+DATA(8)
A
08
03+05=08

## Slide 46: ACI
Opcode | Operand | Description
ACI | 8-bit data | Add immediate to accumulator with carry
The 8-bit data and the Carry Flag (CY) are added to the contents of accumulator.
The result is stored in accumulator.
All flags are modified to reflect the result of the addition.
Example: ACI 45 H

## Slide 47
CY | 1
A | 05
AFTER EXECUTION
BEFORE EXECUTION
ACI 20H A=A+DATA (8)+CY
A
26
05+20+1=26

## Slide 48: DAD
Opcode | Operand | Description
DAD | Reg. pair | Add register pair to H-L pair
The 16-bit contents of the register pair are added to he contents of H-L pair.
The result is stored in H-L pair.
If the result is larger than 16 bits, then CY is set.
No other flags are changed.
Example: DAD B or DAD D

## Slide 49: BEFORE EXECUTION
D | 12 | E | 34
H | 23 | L | 45
D | 12 | E | 34
H | 35 | L | 79
AFTER EXECUTION
DAD D
DAD D DAD B
HL=HL+DE HL=HL+BC
1234
2345 +
------- 3579

## Slide 50: Subtraction
Any 8-bit number, or the contents of register, or the contents of memory location can be subtracted from the contents of accumulator.
The result is stored in the accumulator.
Subtraction is performed in 2’s complement form.
If the result is negative, it is stored in 2’s complement form.
No two other 8-bit registers can be subtracted directly.
collected by C.Gokul AP/EEE,VCET

## Slide 51: SUB
Opcode | Operand | Description
SUB | R M | Subtract register or memory from accumulator
The contents of the register or memory location are subtracted from the contents of the accumulator.
The result is stored in accumulator.
If the operand is memory location, its address is specified by H-L pair.
All flags are modified to reflect the result of subtraction.
Example: SUB B or SUB M

## Slide 52
04
BEFORE EXECUTION
B
C
D
E
H 20 L
50
C
E
50
AFTER EXECUTION
BEFORE EXECUTION
A | 09 |  | 
B | C |  | 04
D | E |  | 
H | L |  | 
AFTER EXECUTION
05
C
D E
H L
SUB C A=A-C
SUB M A=A-M
10
10
2050
2050
A
14
A
B
04
09-04=05
D
H 20 L
14-10=04

## Slide 53: SBB
Opcode | Operand | Description
SBB | R M | Subtract register or memory from accumulator with borrow
The contents of the register or memory location and Borrow Flag (i.e. CY) are subtracted from the contents of the accumulator.
The result is stored in accumulator.
If the operand is memory location, its address is specified by H-L pair.
All flags are modified to reflect the result of subtraction.
Example: SBB B or SBB M

## Slide 54
B
C
05
D
E
H
L
A
08
B
C
05
D
E
A 02
AFTER EXECUTION
BEFORE EXECUTION
SBB C A=A-C-CY
CY
01
CY
1
A
06
A
H
20
L
50
H
03
20 L
50
SBB M
A=A-M-CY
AFTER EXECUTION
BEFORE EXECUTION
02
02
2050H
2050H
H L
08-05-01=02
06-02-1=03

## Slide 55: SUI
Opcode | Operand | Description
SUI | 8-bit data | Subtract immediate from accumulator
The 8-bit data is subtracted from the contents of the accumulator.
The result is stored in accumulator.
All flags are modified to reflect the result of subtraction.
Example: SUI 05H

## Slide 56
A
08
AFTER EXECUTION
BEFORE EXECUTION
SUI 05H
A=A-DATA(8)
A
03
08-05=03

## Slide 57: SBI
Opcode
Operand
Description
SBI
8-bit data
Subtract immediate from accumulator with borrow
The 8-bit data and the Borrow Flag (i.e. CY) is subtracted from the contents of the accumulator.
The result is stored in accumulator.
All flags are modified to reflect the result of subtraction.
Example: SBI 45 H

## Slide 58
CY | 1
A | 25
AFTER EXECUTION
BEFORE EXECUTION
SBI 20H A=A-DATA (8)-CY
A
04
25-20-01=04

## Slide 59: Increment / Decrement
The 8-bit contents of a register or a memory location can be incremented or decremented by 1.
The 16-bit contents of a register pair can be incremented or decremented by 1.
Increment or decrement can be performed on any register or a memory location.

## Slide 60: INR
Opcode | Operand | Description
INR | R M | Increment register or memory by 1
The contents of register or memory location are incremented by 1.
The result is stored in the same place.
If the operand is a memory location, its address is specified by the contents of H-L pair.
Example: INR B or INR M

## Slide 61
B
10
C
D
E
H
L
A
B | 11 | C
D E |  | 
H L |  | 
A
AFTER EXECUTION
H
20
L
50
H
20
L
50
10
11
B | 10 | C
D E |  | 
H L |  | 
2050H
2050H
AFTER EXECUTION
BEFORE EXECUTION
INR M
M=M+1
A
BEFORE EXECUTION
INR B R=R+1
10+1=11
10+1=11

## Slide 62: INX
Opcode | Operand | Description
INX | R | Increment register pair by 1
The contents of register pair are incremented by 1.
The result is stored in the same place.
Example: INX H or INX B or INX D

## Slide 63
B
C
D
E
H 10 L 20
SP |  |  | 
B |  | C | 
D |  | E | 
H | 10 | L | 21
AFTER EXECUTION
BEFORE EXECUTION
SP
INX H RP=RP+1
1020+1=1021

## Slide 64: DCR
Opcode | Operand | Description
DCR | R M | Decrement register or memory by 1
The contents of register or memory location are decremented by 1.
The result is stored in the same place.
If the operand is a memory location, its address is specified by the contents of H-L pair.
Example: DCR B or DCR M

## Slide 65
B
C
D
E 19
A
AFTER EXECUTION
A |  | 
B | C | 
D | E | 20
H | L | 
BEFORE EXECUTION
DCR E R=R-1
H
20
L
50
H
20
L
50
21
20
2050H
BEFORE EXECUTION
DCR M M=M-1
2050H
21-1=20
H L
20-1=19
AFTER EXECUTION

## Slide 66: DCX
Opcode | Operand | Description
DCX | R | Decrement register pair by 1
The contents of register pair are decremented by 1.
The result is stored in the same place.
Example: DCX H or DCX B or DCX D

## Slide 67: BEFORE EXECUTION
B
C
D
E
H 10 L 21
SP |  |  | 
B |  | C | 
D |  | E | 
H | 10 | L | 20
AFTER EXECUTION
SP
DCX H RP=RP-1

## Slide 68: 3.Logical Instructions
These instructions perform logical operations on data stored in registers, memory and status flags.
The logical operations are:
AND
OR
XOR
Rotate
Compare
Complement

## Slide 69: AND, OR, XOR
Any 8-bit data, or the contents of register, or memory location can logically have
AND operation
OR operation
XOR operation
with the contents of accumulator.
The result is stored in accumulator.

## Slide 70
Opcode | Operand | Description
ANA | R M | Logical AND register or memory with accumulator
The contents of the accumulator are logically ANDed with the contents of register or memory.
The result is placed in the accumulator.
If the operand is a memory location, its address is specified by the contents of H-L pair.
S, Z, P are modified to reflect the result of the operation.
CY is reset and AC is set.
Example: ANA B or ANA M.
collected by C.Gokul AP/EEE,VCET

## Slide 71: BEFORE EXECUTION
B
10
C
D
E
H
L
A
B | 0F | C
D |  | E
H |  | L
A
B | 0F | C
D E |  | 
H L |  | 
0A
ANA B
A=A and R
A AA
CY AC
AFTER EXECUTION
CY 0 AC 1
AFTER EXECUTION
BEFORE EXECUTION
CY
AC
CY 0 AC 1
A
11
A
55
H 20 L
50
H 20 L 50
B3
B3
2050H
ANA M
A=A and M
2050H
1010 1010=AAH
0000 1111=0FH
0000 1010=0AH
0101 0101=55H
1011 0011=B3H
0001 0001=11H

## Slide 72
Opcode | Operand | Description
ANI | 8-bit data | Logical AND immediate with accumulator
The contents of the accumulator are logically ANDed with the 8-bit data.
The result is placed in the accumulator.
S, Z, P are modified to reflect the result.
CY is reset, AC is set.
Example: ANI 86H.

## Slide 73: BEFORE EXECUTION
CY
AC
A
B3
AFTER EXECUTION
CY
0
AC
1
33
ANI 3FH
A=A and DATA(8) A
1011 0011=B3H
0011 1111=3FH
0011 0011=33H

## Slide 74
Opcode | Operand | Description
ORA | R M | Logical OR register or memory with accumulator
The contents of the accumulator are logically ORed with the contents of the register or memory.
The result is placed in the accumulator.
If the operand is a memory location, its address is specified by the contents of H-L pair.
S, Z, P are modified to reflect the result.
CY and AC are reset.
Example: ORA B or ORA M.

## Slide 75: 1010 1010=AAH 0001 0010=12H
AFTER EXECUTION
BEFORE EXECUTION
CY AC
ORA B
A=A or R
1011 1010=BAH
B
12 C
D
E
H
L
A
AA
B
12 C
D
E
H
L
A
BA
CY 0 AC 0

## Slide 76
AFTER EXECUTION
BEFORE EXECUTION
CY AC
ORA M
A=A or M
0101 0101=55H
1011 0011=B3H
1111 0111=F7H
H 20 L
50
A
55
A
F7
CY
0
AC 0
H 20 L
50
B3
B3
2050H
2050H

## Slide 77
Opcode | Operand | Description
ORI | 8-bit data | Logical OR immediate with accumulator
The contents of the accumulator are logically ORed with the 8-bit data.
The result is placed in the accumulator.
S, Z, P are modified to reflect the result.
CY and AC are reset.
Example: ORI 86H.

## Slide 78: 1011 0011=B3H 0000 1000=08H
CY
AC
A
B3
AFTER EXECUTION
BEFORE EXECUTION
CY | 0 | AC 0 | 
A | BB |  | 
ORI 08H
A=A or DATA(8)
1011 1011=BBH

## Slide 79
Opcode | Operand | Description
XRA | R M | Logical XOR register or memory with accumulator
The contents of the accumulator are XORed with the contents of the register or memory.
The result is placed in the accumulator.
If the operand is a memory location, its address is specified by the contents of H-L pair.
S, Z, P are modified to reflect the result of the operation.
CY and AC are reset.
Example: XRA B or XRA M.

## Slide 80: BEFORE EXECUTION
B
10
C
D
E
H
L
A
B
C
2D
D
E
H
L
A
87
AFTER EXECUTION
XRA C
A=A xor R
B
C
2D
D
E
H
L
A
AA
CY
AC
CY 0 AC 0
1010 1010=AAH
0010 1101=2DH
1000 0111=87H

## Slide 81: BEFORE EXECUTION
H 20 L
50
A
55
AFTER EXECUTION
XRA M
A=A xor M
CY
AC
CY 0 AC 0
0101 0101=55H
1011 0011=B3H
1110 0110=E6H
H 20 L
50
A
E6
B3
B3
2050H
2050H

## Slide 82
Opcode | Operand | Description
XRI | 8-bit data | XOR immediate with accumulator
The contents of the accumulator are XORed with the 8-bit data.
The result is placed in the accumulator.
S, Z, P are modified to reflect the result.
CY and AC are reset.
Example: XRI 86H.

## Slide 83: 1011 0011=B3H 0011 1001=39H
CY
AC
A
B3
AFTER EXECUTION
BEFORE EXECUTION
CY | 0 | AC 0 | 
A | 8A |  | 
XRI 39H
A=A xor DATA(8)
1000 1010=8AH

## Slide 84: Compare
Any 8-bit data, or the contents of register, or memory location can be compares for:
Equality
Greater Than
Less Than
with the contents of accumulator.
The result is reflected in status flags.

## Slide 85
Opcode | Operand | Description
CMP | R M | Compare register or memory with accumulator
The contents of the operand (register or memory) are compared with the contents of the accumulator.
Both contents are preserved .

## Slide 86
B
10
C
D
E
H
L
A
A | 10 | 
B C |  | 
D | 20 | E
H L |  | 
CY | 01 | Z | 0
A | 10 |  | 
B |  | C | 
D | 20 | E | 
H |  | L | 
AFTER EXECUTION
CMP D A-R
BEFORE EXECUTION
CY Z
AFTER EXECUTION
BEFORE EXECUTION
CY
Z
CY 0
ZF
1
A
B8
H 20 L
50
H 20 L 50
B8
B8
2050H
CMP M A-M
A B8 2050H
A>R: CY=0 A=R: ZF=1 A<R: CY=1
A>M: CY=0 A=M: ZF=1 A<M: CY=1
10<20:CY=01
B8=B8 :ZF=01

## Slide 87
Opcode | Operand | Description
CPI | 8-bit data | Compare immediate with accumulator
The 8-bit data is compared with the contents of accumulator.
The values being compared remain unchanged.

## Slide 88
CY
Z
A
BA
AFTER EXECUTION
BEFORE EXECUTION
CY | 0 | AC 0 | 
A | BA |  | 
CPI 30H A-DATA
A>DATA: CY=0 A=DATA: ZF=1 A<DATA: CY=1
BA>30 :
CY=00

## Slide 89: Rotate
Each bit in the accumulator can be shifted either left or right to the next position.

## Slide 90
Opcode | Operand | Description
RLC | None | Rotate accumulator left
Each binary bit of the accumulator is rotated left by one position.
Bit D7 is placed in the position of D0 as well as in the Carry flag.
CY is modified according to bit D7.
S, Z, P, AC are not affected.
Example: RLC.

## Slide 91
B7
B6
B5
B4
B3
B2
B1
B0
CY
B6 B5 B4 B3 B2 B1 B0 B7
B7
AFTER EXECUTION
BEFORE EXECUTION

## Slide 92
Opcode | Operand | Description
RRC | None | Rotate accumulator right
Each binary bit of the accumulator is rotated right by one position.
Bit D0 is placed in the position of D7 as well as in the Carry flag.
CY is modified according to bit D0.
S, Z, P, AC are not affected.
Example: RRC.

## Slide 93: BEFORE EXECUTION
B7
B6
B5
B4
B3
B2
B1
B0
CY
B0 B7 B6 B5 B4 B3 B2 B1
B0
AFTER EXECUTION
collected by C.Gokul AP/EEE , Velalar college of Engineering and Technology, Erode

## Slide 94
Opcode | Operand | Description
RAL | None | Rotate accumulator left through carry
Each binary bit of the accumulator is rotated left by one position through the Carry flag.
Bit D7 is placed in the Carry flag, and the Carry flag is placed in the least significant position D0.
CY is modified according to bit D7.
S, Z, P, AC are not affected.
Example: RAL.

## Slide 95
B7 B6 B5 B4 B3 B2 B1 B0
CY
B6 B5 B4 B3 B2 B1 B0 CY
B7
AFTER EXECUTION
BEFORE EXECUTION

## Slide 96
Opcode | Operand | Description
RAR | None | Rotate accumulator right through carry
Each binary bit of the accumulator is rotated right by one position through the Carry flag.
Bit D0 is placed in the Carry flag, and the Carry flag is placed in the most significant position D7.
CY is modified according to bit D0.
S, Z, P, AC are not affected.
Example: RAR.

## Slide 97
B7
B6
B5
B4
B3
B2
B1
B0
CY
CY B7 B6 B5 B4 B3 B2 B1
B0
AFTER EXECUTION
BEFORE EXECUTION

## Slide 98: Complement
The contents of accumulator can be complemented.
Each 0 is replaced by 1 and each 1 is replaced by 0.

## Slide 99
Opcode | Operand | Description
CMA | None | Complement accumulator
The contents of the accumulator are complemented.
No flags are affected.
A
00
A
FF
Example: CMA. A=A’
BEFORE EXECUTION
AFTER EXECUTION

## Slide 100
Opcode | Operand | Description
CMC | None | Complement carry
The Carry flag is complemented.
No other flags are affected.
Example: CMC => c=c’
BEFORE EXECUTION
AFTER EXECUTION
C
00
C
FF

## Slide 101
Opcode | Operand |  | Description
STC | None | Set carry | 
The Carry flag is set to 1.
No other flags are affected.
Example: STC CF=1
S-set (1)
C-clear (0)

## Slide 102
The branch group instructions allows the microprocessor to change the sequence of program either conditionally or under certain test conditions. The group includes,
(1) Jump instructions,
(2) Call and Return instructions,
(3) Restart instructions,

## Slide 103
Opcode | Operand | Description
JMP | 16-bit address | Jump unconditionally
The program sequence is transferred to the memory location specified by the 16-bit address given in the operand.
Example: JMP 2034 H.

## Slide 104
Opcode | Operand | Description
Jx | 16-bit address | Jump conditionally
The program sequence is transferred to the memory location specified by the 16-bit address given in the operand based on the specified flag of the PSW.
Example: JZ 2034 H.

## Slide 105: Jump Conditionally
Opcode | Description | Status Flags
JC | Jump if Carry | CY = 1
JNC | Jump if No Carry | CY = 0
JZ | Jump if Zero | Z = 1
JNZ | Jump if No Zero | Z = 0
JPE | Jump if Parity Even | P = 1
JPO | Jump if Parity Odd | P = 0
A-Above , B-Below , C-Carry , Z-Zero , P-Parity

## Slide 106
Opcode | Operand | Description
CALL | 16-bit address | Call unconditionally
The program sequence is transferred to the memory location specified by the 16-bit address given in the operand.
Before the transfer, the address of the next instruction after CALL (the contents of the program counter) is pushed onto the stack.
Example: CALL 2034 H.

## Slide 107: Call Conditionally
Opcode | Description | Status Flags
CC | Call if Carry | CY = 1
CNC | Call if No Carry | CY = 0
CP | Call if Positive | S = 0
CM | Call if Minus | S = 1
CZ | Call if Zero | Z = 1
CNZ | Call if No Zero | Z = 0
CPE | Call if Parity Even | P = 1
CPO | Call if Parity Odd | P = 0

## Slide 108
Opcode | Operand | Description
RET | None | Return unconditionally
The program sequence is transferred from the subroutine to the calling program.
The two bytes from the top of the stack are copied into the program counter, and program execution begins at the new address.
Example: RET.

## Slide 109: Return Conditionally
Opcode | Description | Status Flags
RC | Return if Carry | CY = 1
RNC | Return if No Carry | CY = 0
RP | Return if Positive | S = 0
RM | Return if Minus | S = 1
RZ | Return if Zero | Z = 1
RNZ | Return if No Zero | Z = 0
RPE | Return if Parity Even | P = 1
RPO | Return if Parity Odd | P = 0

## Slide 110
Opcode | Operand | Description
RST | 0 – 7 | Restart (Software Interrupts)
The RST instruction jumps the control to one of eight memory locations depending upon the number.
These are used as software instructions in a program to transfer program execution to one of the eight locations.
Example: RST 1 or RST 2 ….

## Slide 111
Instruction Code | Vector Address
RST 0 | 0*8=0000H
RST 1 | 1*8=0008H
RST 2 | 2*8=0010H
RST 3 | 3*8=0018H
RST 4 | 4*8=0020H
RST 5 | 5*8=0028H
RST 6 | 6*8=0030H
RST 7 | 7*8=0038H

## Slide 112: 5. Control Instructions
The control instructions control the operation of microprocessor.
collected by C.Gokul AP/EEE , Velalar college of Engineering and Technology, Erode

## Slide 113
Opcode | Operand | Description
NOP | None | No operation
No operation is performed.
The instruction is fetched and decoded but no operation is executed.
Example: NOP

## Slide 114
Opcode | Operand |  | Description
HLT | None | Halt | 
The CPU finishes executing the current instruction and halts any further execution.
An interrupt or reset is necessary to exit from the halt state.
Example: HLT

## Slide 115
Opcode | Operand | Description
DI | None | Disable interrupt
The interrupt enable flip-flop is reset and all the interrupts except the TRAP are disabled.
No flags are affected.
Example: DI

## Slide 116
Opcode | Operand | Description
EI | None | Enable interrupt
The interrupt enable flip-flop is set and all interrupts are enabled.
No flags are affected.
This instruction is necessary to re-enable the interrupts (except TRAP).
Example: EI

## Slide 117
Opcode | Operand | Description
RIM | None | Read Interrupt Mask
This is a multipurpose instruction used to read the status of interrupts 7.5, 6.5, 5.5 and read serial data input bit.
The instruction loads eight bits in the accumulator with the following interpretations.
Example: RIM

## Slide 118: RIM Instruction

## Slide 119
Opcode | Operand | Description
SIM | None | Set Interrupt Mask
This is a multipurpose instruction and used to implement the 8085 interrupts 7.5, 6.5, 5.5, and serial data output.
The instruction interprets the accumulator contents as follows.
Example: SIM

## Slide 120: SIM Instruction