## Slide 1: RISC Vs CISC, Harvard v/s Van Neumann

## Slide 2: CISC Architecture
 The simplest way to
advantages and disadvantages
examine the
of
RISC architecture is by contrasting it with it's predecessor: CISC (Complex Instruction Set Computers) architecture.

## Slide 3: Multiplying Two numbers in Memory
On the right is a diagram representing the storage scheme for a generic computer. The main memory is divided into locations numbered from (row) 1: (column) 1 to (row) 6:
(column) 4.

## Slide 4: Multiplying Two numbers in Memory
The execution unit is responsible for carrying out all computations. However, the execution unit can only operate on data that has been loaded into one of the six registers (A, B, C, D, E, or F).

## Slide 5: Multiplying Two numbers in Memory
Let's say we want to find the product of two numbers - one stored in location 2:3 and another stored in location 5:2 - and then store the product back in the location 2:3.

## Slide 6: The CISC Approach
The primary goal of CISC architecture is to complete a task in as few lines of assembly as possible.
This is achieved by building processor hardware that is capable of understanding and executing a series of operations.

## Slide 7: The CISC Approach
For this particular task, a CISC processor would come prepared with a specific instruction (we'll call it "MULT").
When executed, this instruction loads the two values into separate registers, multiplies the operands in the execution unit, and then stores the product in the appropriate register.
Thus, the entire task of multiplying two numbers can be completed with one instruction:
MULT 2:3, 5:2

## Slide 8: The CISC Approach
MULT is what is known as a "complex instruction."
It operates directly on the computer's memory banks and does not require the programmer to explicitly call any loading or storing functions.
It closely resembles a command in a higher level language.
For instance, if we let "a" represent the value of 2:3 and "b" represent the value of 5:2, then this command is identical to the C statement "a = a * b."

## Slide 9: The CISC Approach
One of the primary advantages of this system is that the compiler has to do very little work to translate a high-level language statement into assembly.
Because the length of the code is relatively short, very little RAM is required to store instructions.
The emphasis is put on building complex instructions directly into the hardware.

## Slide 10: The RISC Approach
RISC processors only use simple instructions that can be executed within one clock cycle.
Thus, the "MULT" command described above could be divided into three separate commands: "LOAD," which moves data from the memory bank to a register, "PROD," which finds the product of two operands located within the registers, and "STORE," which moves data from a register to the memory banks.

## Slide 11: The RISC Approach
 In order to perform the exact series of steps described in the CISC approach, a programmer would need to code four lines of assembly:
LOAD A, 2:3
LOAD B, 5:2 PROD A, B STORE 2:3, A

## Slide 12: The RISC Approach
At first, this may seem like a much less efficient way of completing the operation.
Because there are more lines of code, more RAM is needed to store the assembly level instructions.
The compiler must also perform more work to convert a high-level language statement into code of this form.

## Slide 13: The RISC Approach
However, the RISC strategy also brings some very important advantages.
Because each instruction requires only one clock cycle to execute, the entire program will execute in approximately the same amount of time as the multi-cycle "MULT" command.
These RISC "reduced instructions" require less transistors of hardware space than the complex instructions, leaving more room for general purpose registers.
Because all of the instructions execute in a uniform amount of time (i.e. one clock), pipelining is possible.

## Slide 14: CISC
1.Emphasis on hardware
RISC
1.Emphasis on software
2.Includes multi-clock
complex instructions
2.Single-clock,
reduced instruction only
3.Memory-to-memory: "LOAD" and "STORE"
incorporated in instructions
3.Register to register: "LOAD" and "STORE"
are independent instructions
4.Small code sizes, high cycles per second
4.Low cycles per second, large code sizes
5.Transistors used for storing
complex instructions
5.Spends more transistors
on memory registers
http://cs.stanford.edu/people/eroberts/courses/soco/projects/risc/developments/index.html

## Slide 15: Harvard Architecture
The name Harvard Architecture comes from the Harvard Mark I relay-based computer.
The Harvard architecture is a computer architecture with physically separate storage and signal pathways for instructions and data.

## Slide 16: Harvard Architecture
In other words, it physically separate signals and storage for code/program and data memory.
It is possible to access program memory and data memory simultaneously.
Typically, code (or program) memory is read-only and data memory is read- write.
Therefore, it is impossible for program contents to be modified by the
program itself.
R.K.Tiwari(ravikumar.tiwari@raisoni.net)

## Slide 17: Von Neumann Architecture
The von Neumann Architecture is named after the mathematician and early computer scientist John von Neumann.
Von Neumann machines have shared signals and memory for code and data.
Thus, the program can be easily modified by itself since it is stored in read-write memory.

## Slide 18: VAN-NEUMANN ARCHITECTURE
HARVARD ARCHITECTURE
Used in conventional processors found in PCs and Servers, and embedded systems with only control functions.
Used in DSPs and other processors found in latest embedded systems and Mobile communication systems, audio, speech, image processing systems
The data and program are stored The data and program memories
in the same memory are separate
The code is executed serially and The code is executed in parallel takes more clock cycles
There is no exclusive Multiplier
It has MAC (Multiply Accumulate)
Absence of Barrel Shifter
Barrel Shifter help in shifting and rotating operations of the data
The programs can be optimized in The program tend to grow big in
lesser size size
R.K.Tiwari(ravikumar.tiwari@raisoni.net)

## Slide 19: Microcontrollers
Embedded Systems
  Operations managed behind the scenes by a microcontroller
Microcontroller (MCU)
  Integrated electronic computing device that includes three major components on a single chip
    Microprocessor (MPU)
    Memory
    I/O (Input/Output) ports

## Slide 20: Microcontrollers
Support Devices
  Timers
  A/D converter
  Serial I/O
Common communication lines
  System Bus

## Slide 21: MCU-Based System

## Slide 22: Software
Machine Language
  Binary Instructions
  Difficult to decipher and write
 Error-prone
  All programs converted into machine language for execution
Instruction | Hex | Mnemonic | Description | Processor
10000000 | 80 | ADD B | Add reg B to Acc | Intel 8085
00101000 | 28 | ADD A, R0 | Add Reg R0 to Acc | Intel 8051
00011011 | 1B | ABA | Add Acc A and B | Motorola 6811

## Slide 23: Software
Assembly Language
  Machine instructions represented in mnemonics
  One-to-one correspondence
  Efficient execution and use of memory
  Machine-specific

## Slide 24: Evolution of Programming
Machine Language
  Binary format
11100101100111110001000000010000
11100101100111110000000000001000
11100000100000010101000000000000
11100101100011110101000000001000
  Hexadecimal format E59F1010 E59F0008
E0815000
E58F5008

## Slide 25: Evolution of Programming
Assembly Language
  Mnemonic codes
E59F1010 | LDR | R1, | num1
E59F0008 | LDR | R0, | num2
E0815000 | ADD | R5, | R1, R0
E58F5008 | STR | R5, | sum
High-Level Language
  C language
sum = num1 + num2;

## Slide 26: Approaches
Machine Independent
Machine Dependent
Human Readable
High-Level Languages (C, C++, Java, Pascal)
Assembly Languages
Human Unreadable
Pseudo Code (Bytecode, P-code)
Machine Languages (x86, MIPS, ARM)

## Slide 27: From Source to Executable
Preprocessor
Preprocessed Code
Compiler
Assembly Code
Assembler
Source Code Object Code
Linker
Executable Code
Loader
Debugger
Libraries

## Slide 28: Compiler, Assembler, Linker, Cross Compiler...

## Slide 29: Compiler
A software program that converts source code that written in high level programming language into low level language.
A Native-compiler runs on a computer platform and produces code for that same computer platform.
A Cross-compiler runs on one computer platform and produces code for another computer platform.

## Slide 30: Assembler
 Convert assembly into object file

## Slide 31: Linker
A linker or link editor is a program that takes one or more objects generated by compilers and assembles them into a single executable program or a library that can later be linked to in itself.
Link the object files and libraries to form an executable

## Slide 32: Cross-Compiler
A cross compiler is a compiler capable of creating executable code for a platform other than the one on which the compiler is running.
For example, a compiler that runs on a Windows 7 PC but generates code that runs on Android smartphone is a cross compiler.

## Slide 33: Debugger
A debugger or debugging tool is a computer program that is used to test and debug other programs.
The code to be examined might alternatively be running on an instruction set simulator .
When the program crashes, the debugger shows the actual position(Segment) in the original code if it is a source-level debugger.
If it is a low-level debugger or a machine- language debugger it shows that line in the program.

## Slide 34: Emulator
An emulator is a piece of Hardware/Software that enables one computer system to run programs that are written for another computer system.
For example emulator 8086, 8086 microprocessor programs.
An emulator is used on the target processor (the processor for which the program is being written).

## Slide 35: Emulator Example
Android Virtual Machine(AVM)