## Slide 1: Arithmetic Pipeline

## Slide 2
Main topics in Pipeline processing is
  Arithmetic pipeline :
    fixed Arithmetic pipeline
    floating point
  Vector processing : adder/multiplier pipeline
  Array processing : array processor
    Attached array processor
    SIMD Array Processor

## Slide 3: Parallel Processing
Adder-subtractor
Integer multiply
Floatint-point add-subtract
Incrementer
Shift unit
Logic unit
Floatint-point divide
Floatint-point multiply
Processor registers
To Memory
Simultaneous data processing tasks for the purpose of increasing the computational speed
Perform concurrent data processing to achieve faster execution time
Multiple Functional Unit :
  Separate the execution unit into eight functional units operating in parallel.

## Slide 4: Pipelining: Laundry Example
A B C D
Small laundry has one washer, one dryer and one operator, it takes 90 minutes to finish one load:
  Washer takes 30 minutes
  Dryer takes 40 minutes
  “operator folding” takes 20 minutes

## Slide 5: Sequential Laundry
A
B
C
D
30 40 20 30 40 20 30 40 20 30 40 20
6 PM
7 8
9
Time
10
11
Midnight •
T
a s k
O
r d e r
90 min
This operator scheduled his loads to be delivered to the laundry every 90 minutes which is the time required to finish one load.
In other words he will not start a new task unless he is already done with the previous task
The process is sequential. Sequential laundry takes 6 hours for 4 loads

## Slide 6: Efficiently scheduled laundry: Pipelined Laundry Operator
A
B
C
D
6 PM
7 8
9 10 11
Time
T
a s k
O
r d e r
30 40 40 40 40 20
40 40 40
Another operator asks for the delivery of loads to the laundry every 40 minutes!?.
Pipelined laundry takes 3.5 hours for 4 loads

## Slide 7: Pipelining Facts
Multiple tasks operating simultaneously
Pipelining doesn’t help latency (response time) of single task, it helps throughput of entire workload
Pipeline rate limited by slowest pipeline stage
Potential speedup = Number of
pipe stages
Unbalanced lengths of pipe stages reduces speedup
A
B
C
D
T
a s k
O
r d e r
6 PM | 7 |  | 8 | 9
 |  |  |  | Time
30 | 40 | 40 | 40 | 40 20
The washer waits for the dryer for 10 minutes

## Slide 8: Pipelining
Decomposing a sequential process into suboperations
Each subprocess is executed in a special dedicated segment concurrently
Instruction execution is divided into k segments or stages
  Instruction exits pipe stage k-1 and proceeds into pipe stage k
  All pipe stages take the same amount of time; called one processor cycle
  Length of the processor cycle is determined by the slowest pipe stage
k segments

## Slide 9: Pipelining
Suppose we want to perform the combined multiply and add operations with a stream of numbers:
Ai * Bi + Ci for i =1,2,3,…,7
The sub operations performed in each segment of the pipeline are as follows:
R1  Ai ,
R2  Bi
R3  R1 * R2 R4  Ci
R5  R3 + R4

## Slide 11: Arithmetic Pipeline
Pipeline arithmetic units are usually found in very high speed computers.
Arithmetic pipelines are constructed for : simple fixed-point
floating-point arithmetic operations.
For implementing the arithmetic pipelines we generally use following two types of adder:
i) Carry propagation adder (CPA): It adds two numbers such that carries generated in successive digits are propagated.
ii) Carry save adder (CSA): It adds two numbers such that carries generated are
not propagated rather these are saved in a carry vector.

## Slide 12: Fixed Arithmetic pipeline
We take the example of multiplication of fixed numbers.
Two fixed-point numbers are added by the ALU using add and shift operations.
This sequential execution makes the multiplication a slow process.
Observe that this is the process of adding the multiple copies of shifted multiplicands as show below:

## Slide 13: Fixed Arithmetic pipeline

## Slide 14: Now, we can identify the following stages for the pipeline:
The first stage generates the partial product of the numbers, which form the six rows of shifted multiplicands.
In the second stage, the six numbers are given to the two CSAs merging into four numbers.
In the third stage, there is a single CSA merging the numbers into 3numbers.
In the fourth stage, there is a single number merging three numbers into
2numbers.
In the fifth stage, the last two numbers are added through a CPA to get the final product.

## Slide 16: Floating point operations.
The inputs to floating point adder pipeline are two normalized floating point numbers.
A and B are mantissas and a and b are the exponents.
The floating point addition and subtraction can be performed in four segments.
Exponent
Mantissa

## Slide 17: Floating-Point Add/Subtraction Pipeline:
Exponent
Mantissa

## Slide 20: Vector Processing
Science and Engineering Applications
  Long-range weather forecasting,
  Petroleum explorations,
  Seismic data analysis
  Medical diagnosis ,
  Aerodynamics and space flight simulators,
  Artificial intelligence and expert systems,
  Mapping the human genome, Image processing

## Slide 21: Vector Processing

## Slide 22: Vector Instruction Format :
100
ADD A B C
Matrix Multiplication
3 x 3 matrices multiplication : n2 = 9 inner product
: inner product 9
Cumulative multiply-add operation : n3 = 27 multiply-add
: Three such multiply-add
therefore 9 X 3 multiply-add = 27
Operation code | Base address source 1 | Base address source 2 | Base address destination | Vector length


 
21
21 22 23 
c c
c12 c13 
21 22 23 
c32 c33 
23 
b33  c31
b   c
b
  b
b12 b13  c11
22
b32
a31 a32 a33  b31
a a
a
a11 a12 a13  b11
c11  a11 b11  a12 b21  a13 b31
c  c  a  b
C11 initial value = 0
c11  c11  a11 b11  a12 b21  a13 b31
     

## Slide 23
Pipeline for calculating an inner product :
  Floating point multiplier pipeline : 4 segment
  Floating point adder pipeline : 4 segment
Example:
after 1st clock input
after 8th clock input
The four partial sum are added to form the final sum
C  A1B1  A2 B2  A3B3   Ak Bk
Source A
Source B
Multiplier
pipeline
Adder
pipeline
after 4th clock input
A
1B1
Source A
Source B
Multiplier
Adder
pipeline pipeline
A4B4
A3B3
A2B
2 A1B
1
Source A
Source B
Multiplier
pipeline
Adder
pipeline
Source A
Source B
Multiplier
pipeline
Adder
pipeline
after 9th, 10th, 11th ,...
8B8
A A7B7 A6B
6 A5B
5
A4B4
A3B
3 A2
B2 A1B1
A8B8
A7B7
A6B
6 A5B
5
A4B4
A3B3
A2B
2 A1B
1
A1B1  A5B5
, , ,  
A2 B2  A6B6
 A4 B4  A8 B8  A12B12  A16B16 
 A3B3  A7 B7  A11B11  A15B15 
 A2 B2  A6 B6  A10B10  A14B14 
C  A1B1  A5B5  A9 B9  A13B13 

## Slide 24: Memory Interleaving
Memory Interleaving :
  Simultaneous access to memory from two or more source using one memory bus system.
  Select one of 4 memory modules using lower 2 bits of AR
  Example) Even / Odd Address Memory Access
Address bus |  |  |  | 
AR AR AR AR Memory Memory Memory Memory array array array array DR DR DR DR |  |  |  | 
Data bus |  |  |  | 

## Slide 25: Array Processor
Processor that performs the computations on large arrays of data.
Vector processing : Adder/Multiplier pipeline use Array processing: using a separate array processor
There are two different types of (array processor) :
  Attached Array Processor
  SIMD Array Processor

## Slide 26: Attached Array Processor
It is designed as a peripheral for a conventional host computer.
Its purpose is to enhance the performance of the computer by providing vector processing.
It achieves high performance by means of parallel processing with multiple functional units.
General-purpose computer
Input-Output interface
Attached array Processor
Main memory
Local memory
High-speed memory to- memory bus

## Slide 27: SIMD Array Processor
It is processor which consists of multiple processing unit operating in parallel.
The processing units are synchronized to perform the same task under control of common control unit.
Each processor elements(PE) includes an ALU , a floating point arithmetic unit and working register.
PE 1
PE 3
PE 2
M1
M3
M2
PE n
Mn
Master control unit
Main memory