## Slide 1




Flynn’s Classification Of Computer
Architectures
In 1966, Michael Flynn proposed a classification for computer architectures based on the number of instruction steams and data streams (Flynn’s Taxonomy).
Flynn uses the stream concept for describing a machine's structure
A stream simply means a sequence of items (data or instructions).
The classification of computer architectures based on the number of instruction steams and data streams (Flynn’s Taxonomy).

## Slide 2
Flynn Classification Of
Computer architectures
Flynn’s Taxonomy




SISD: Single instruction single data
– Classical von Neumann architecture
SIMD: Single instruction multiple data
MISD: Multiple instructions single data– Non existent, just listed for completeness
MIMD: Multiple instructions multiple data – Most common and general parallel machine

## Slide 3


SISD
SISD (Singe-Instruction stream, Singe-Data stream)
SISD corresponds to the traditional mono- processor ( von Neumann computer). A single data stream is being processed by one
instruction stream
OR

A single-processor computer (uni-processor) in which a single stream of instructions is generated from the program.

## Slide 4
SISD
where CU= Control Unit, PE= Processing Element, M= Memory

## Slide 5




SIMD
SIMD (Single-Instruction stream, Multiple- Data streams)
Each instruction is executed on a different set of data by different processors i.e multiple processing units of the same type process on multiple-data streams.
This group is dedicated to array processing machines.
Sometimes, vector processors can also be seen as a part of this group.

## Slide 6
SIMD
where CU= Control Unit, PE= Processing Element, M= Memory

## Slide 7




MISD
MISD (Multiple-Instruction streams, Singe- Data stream)
Each processor executes a different sequence of instructions.
In case of MISD computers, multiple processing units operate on one single-data stream .
In practice, this kind of organization has never been used

## Slide 8
MISD
where CU= Control Unit, PE= Processing Element, M= Memory

## Slide 9





MIMD
MIMD (Multiple-Instruction streams,
Multiple- Data streams)
Each processor has a separate program.
An instruction stream is generated from each program.
Each instruction operates on different data. This last machine type builds the group for the traditional multi-processors. Several processing units operate on multiple-data streams.

## Slide 10
MIMD Diagram