## Slide 1
Instruction formats

## Slide 2: What is instruction format?
An instruction is normally made up of a combination of an operation code and some way of specifying an operand, most commonly by its location or address in memory

## Slide 3: Types of address instructions
Three address instructions
Memory addresses for the two operands and one destination need to be specified.
It is also called General register organization.
Instruction: ADD R1, R2, R3
Microoperation: R1  R2 + R3

## Slide 4: EVALUATE X=(A+B)*(C+D)
ADD ADD | R1, A, B R2, C, D | R1  M[A]+M[B] R2  M[C]+M[D]
MUL | X, R1, R2 | M[X]  R1*R2
X=A+(B.C)+(D.E)

## Slide 5: Two address instructions
Two address registers or two memory locations are specified
Assumes that the destination address is the same as that of the first operand.
Instruction: ADD R1, R2 Microoperation: R1  R1 + R2

## Slide 6: EVALUATE X=(A+B)*(C+D)
MOV | R1, A | R1  M[A]
ADD | R1, B | R1  R1+M[B]
MOV | R2, C | R2  M[C]
ADD | R2, D | R2  R2+M[D]
MUL | R1,R2 | R1  R1*R2
MOV | X,R1 | M[X]  R1
X=A+(B.C)+(D.E)

## Slide 7: One address instructions
One address can be a register name or memory address.
SINGLE ACCUMULATOR ORGANIZATION
It uses AC register for all data manipulation
Instruction: ADD X
Microoperation: AC  AC + M[X]

## Slide 8: EVALUATE X=(A+B)*(C+D)
LOAD | A | AC  M[A]
ADD | B | AC  AC+M[B]
STORE | T | M[T]  AC
LOAD | C | AC  M[C]
ADD | D | AC  AC+M[D]
MUL | T | AC  AC*M[T]
STORE | X | M[X]  AC
X=A+(B.C)+(D.E)

## Slide 9: Zero address instruction
Stack is used. Arithmetic operation pops two operands from the stack and pushes the result.
Also called stack organization

## Slide 10: Zero address instruction
•
Evaluate X = ( A +B ) * ( C +D )
PUSH | A | TOS  A | 
PUSH ADD | B | TOS  B TOS  (A+B) | 
PUSH | C | TOS  | C
PUSH | D | TOS  | D
ADD |  | TOS  | (C+D)
MUL |  | TOS  (C+D)*(A+B) | 
POP | X | M[X]  TOS | 
Push A
Push B
ADD
Push C
Push D
ADD
Mult
Store

## Slide 11: Addressing Modes
Addressing mode specifies a rule for interpreting or modifying the address field of the instruction before the operand is actually executed.

## Slide 12: Well known addressing modes-
•
•
•
•
•
•
•
•
•
•
Implied mode Immediate mode Register mode Register indirect mode
Autoincrement or Autodecrement
Direct address mode Indirect address mode Relative address mode Indexed addressing mode
Base register addressing mode

## Slide 13: Implied Mode
In this mode the operands are specified implicitly in the definition of the instruction.
All register reference instructions that use an accumulator are implied mode instruction.
Example: CMA compliment accumulator.

## Slide 14: Immediate Addressing
Data needed by the processor is contained in the instruction
Operand= address field
e.g-ADD 5
-add 5 to the content of accumulator
-5 is the operand
opcode Operand (5)

## Slide 15: Register Addressing
•
Operand is held in register named in address field
A k-bit field can specify any one of 2^k registers
•
OPERAND
REGISTERS
OPCODE | REGISTER ADDRESS R |  | 

## Slide 16: Register Indirect Addressing
The selected register contains the address of the operand rather than the operand itself.
OPERAND(72)
Memory
ADDRESS OF OPERAND(500) | 
OPCODE | REGISTER ADDRESS R | 
 |  | REGISTERS R
500

## Slide 17: Auto Increment or Auto Decrement Mode
•
This is similar to the register indirect mode except that the register is incremented or decremented after or before its value is used to access memory.
R1=400
450
700
399
400
1. Auto incr-E.A=400
R1 is incremented to 401after the execution
2. Auto decr-R1 is decremented prior to the execution,therefore,R1=399 and E.A=399

## Slide 18: RELATIVE ADDRESS MODE
In this mode the content of the program counter is added to the address part of the instruction to obtain the effective address.
OPCODE |  | Address(24) | 
PC (825) |  |  | 
24
MEMORY
826 + Effective 850
Address
826+24

## Slide 19: Indexed addressing mode
In this mode the content of an index register is added to the address part of the instruction to obtain the effective address.
opcode Rb Rt ADDRESS(20)
index register(1000)
operand
+
1020
E.A
1000
20
Memory

## Slide 20: BASE REGISTER ADDRESSING MODE
•
In this mode the content of a base register is added to the address part of the instruction to obtain the effective address.
opcode Rb Rt ADDRESS
REGISTER(400)
42
Memory
100
400
+
500
E.A