## Slide 1: Measuring Performance

## Slide 2: In This Demonstration
What is Performance?
Performance Measurement Methods
MIPS CPI / IPC
Choosing Programs to Evaluate Performance Benchmark Suits
Speedup
Quantitative Principles of Computer Design

## Slide 3: Performance
Performance means
How quickly a given system executes a program/ a set of programs
Two aspects
Response Time
The time between the start and the completion of an event– execution time.
Throughput
The total amount of work done in a given time

## Slide 4: MIPS
Millions of Instructions Per Second
An early measure of computer performance.
MIPS = No. of instruction executed in a program Time required to run the program
typically expressed in millions of instructions per second.
Out Of Use
It does not account for the fact that different systems often require different no.s of instructions to implement a given program.
A computer’s MIPS ratings does not tell you about how many instructions it require to perform a given task.

## Slide 5: CPI / IPC
CPI
Cycle Per Instruction
No of clock cycles required to execute each instruction
CPI = No. of clock cycles required
No. of instructions executed
IPC
Instructions Per Cycle
No. of instructions executed per cycle
IPC = No of Instructions executed No of clock cycles required
Large IPC tends to indicate good performance & large CPI indicates poor performance

## Slide 6: Choosing Programs to Evaluate
Performance
Five levels of programs used to evaluate performance are
Real applications
Compilers, Text-processing S/W like Word, and Photoshop.
Modified ( or scripted) applications
To enhance portability or to focus on one particular aspect of system performance
Kernels
To isolate performance of individual features of a machine.
Toy Benchmarks
Typically between 10- 100 lines if code and produce a result the user already knows.
Synthetic benchmarks
Try to match the average frequency of operations and operands of a large set of programs.

## Slide 7: Benchmark Suits
A set of programs that are believed to be typical of the programs that will be run on the system
System is checked for how long it take to execute all of the programs in the suite.
For example SPEC benchmark by Standard Performance Evaluation Cooperation
Other benchmarks are:
Business Winstone CC Windows Winbench

## Slide 8: Speedup
Speedup tells how the performance of an architecture changes as different improvements are made to architecture
Ratio of the execution times before and after a change is made
Speedup = Execution time old(before)
Execution time new(after)

## Slide 9: Quantitative Principles of Computer Design (Continued)
Some principles that are useful in design and analysis of computers
Make The Common Case Faster Amdahl’s Law
CPU Performance Equation Principles Of Locality
Taking Advantage of Parallelism

## Slide 10: Make the Common Case Fast
In making a design trade-off,
Favor the frequent case over the infrequent case because
The frequent case is often simpler and can be done faster than the infrequent case
e.g. when multiplying two numbers, overflow is the infrequent case, no overflow is the frequent.
However, system will slow down when overflow occurs.
We have to decide what the frequent case is and how much performance can be improved by making that case faster
Amdahl’s law quantify this principle

## Slide 11: Amdahl’s Law
Impact of a given performance improvement on overall performance depends on
How much the improvement improves the performance ( when in use)
How often the improvement is in use
Execution Time new = Execution Time old Fraction unused +Fraction used
Speedup used
Where
Fraction unused = Fraction of time( not instructions) that the improvement is not in use.
Fraction used = Fraction of time that the improvement is in use
Speedup used = Speedup that occurs when the improvement is used

## Slide 12: Amdahl’s Law Continued)
Fraction used and Fraction unused are computed using the execution time before the modification is applied
Speedup can be defined as
Speedup = Execution time old(before)
Execution time new(after)
1
= Fraction unused +Fraction used
Speedup used

## Slide 13: Amdahl’s Law (Continued)
The law states
“ Performance improvement to be gained from using some faster mode of execution is limited by the fraction of the time the faster mode can be used”
Speedup = Performance for entire task using the enhancement Performance for entire task without using the enhancement
Or
Speedup = Execution time for the entire work without using the enhancement Execution time for entire task using the enhancement when possible
Speedup = Execution time old(before)
Execution time new(after)
= 1
(1- Fraction enhanced )+Fraction enhanced
Speedup enhanced

## Slide 14: An Example
Problem.
An enhancement is made to a processor of a server system. The new CPU time is 20 times faster than original. If the original CPU is busy with computation 35% of the time and is waiting for I/O 65% of the time, what is the overall speedup gained by incorporating the enhancement.
Solution.
Fraction enhanced = 35/100=.35.
Speedup enhanced = 20.
= 1
(1- 0.35 )+0.35
20
= 1.498173

## Slide 15: CPU Performance Equation
CPU time = CPU clock cycles for a program x Clock cycle time -------(1)
Clock Cycle Time = 1 Clock rate
(1) Implies
CPU time = CPU clock cycles for a program -------------------(2)
Clock rate
Now, CPI = CPU clock cycles for a program Instruction Count
CPU clock cycle for a program = CPI x IC Now (1) implies
CPU time = CPI x IC x Clock Cycle time ------------(3)

## Slide 16: CPU Performance Equation (Continued)
By putting values equation (3) becomes
CPU time = Instructions x clock cycles x Seconds Program x Instructions x Clock cycles
= Seconds Program
Unfortunately, it is difficult to change one parameter in complete isolation from others because the basic technologies involved in changing each characteristic are interdependent:
Clock Cycle Time = H/W technology and organization CPI = Organization and instruction set architecture
Instruction Count = Instruction set architecture and compiler technology

## Slide 17: Principles of Locality
Programs tend to reuse data and instructions they have used recently
A program spends 90% of its execution time in only 10% of the code
We can predict with reasonable accuracy what instructions and data a program will use in the near future based on its accesses in the recent past.
Two types of locality
Temporal locality
States that recently accessed items are likely to be accessed in the near future.
Spatial Locality
Items whose addresses are near one another tend to be referenced close together in time.

## Slide 18: Taking Advantage of Parallelism
One of the most important methods for improving performance – It is obtained through
Pipelining – to overlap the execution of instructions, so as to reduce the total time to complete a sequence of instructions.

## Slide 19
Research is carried out on various aspects in order to improve performance and reduce cost