## Slide 1
MEMORY ORGANIZATION
1

## Slide 2: MEMORY UNIT
2

## Slide 3: 3 Memory Unit
an essential component in any general purpose computer since it is needed to store programs and data.
memory unit that communicates directly with the CPU = main memory
devices that provide backup storage = auxiliary memory.
Auxiliary memory devices are used to store system programs, large data files and other backup information. Only programs and data currently needed by the processor reside in main memory. All other information is stored in main memory and transferred to main memory when needed.

## Slide 4: Cache Memory
Memory that lies in between main memory and CPU
Holds those parts of the program and data that are most heavily used
increases the overall processing speed of the computer by providing frequently required data to the CPU at a faster speed.
4

## Slide 5: Main Memory
Memory unit that communicates directly with CPU
Programs and data currently needed by the processor reside here
Also known as primary memory
RAM and ROM
5

## Slide 6: Auxiliary Memory
Made of devices that provide backup storage
Magnetic tapes, Magnetic disks
At the bottom of the hierarchy are the relatively slow magnetic tapes used to store removable files whereas at the top level, magnetic disks used as backup storage
6

## Slide 7: 7 Memory Types
Sequential Access Memory
A class of data storage device that read their data in sequence
Are usually a form of magnetic memory
Typically used for secondary storage in general-purpose computers due to their higher density, resistance to wear and non-volatility
Eg: hard disk, CD-ROMs, magnetic tapes etc
Random Access Memory
Is a form of computer data storage
Allows stored data to be accessed in any order
Associated with volatile types of memory
Type: SRAM and DRAM

## Slide 8: Memory Hierarchy
To obtain the highest possible access speed while minimizing the
total cost of the memory system
Consists of all storage device in a computer system (auxiliary, cache, main , high speed registers and processing logic)
8

## Slide 9
9

## Slide 10
Magnetic disk
I/O Processor
Main
Memory
CPU
Cache
Memory
10
Magnetic
tapes
Fig: Memory Hierarchy in a Computer System

## Slide 11: MAIN MEMORY
11

## Slide 12: Main memory
12
Basic memory of the computer
Temprorary memory except ROM
Faster for read write operation
Expensive internal memory so not portable.
RAM
Volatile memory.
Store the information required during processing
Two types of random Static RAM(SRAM) and Dynamic RAM(DRAM)

## Slide 13: TYPES OF RAM
Information is stored in form of
voltage
faster
Loses its content after few
seconds
Information is stored in the
form of charge
slower
SRAM
Does not lose its content until computer is turned off
DRAM
13

## Slide 14: ROM
Permanent memory
Store the information required for computer operations
Types of ROM (PROM,EPROM,EEPROM)
14

## Slide 15: Boot Strap loader
Initial program whose function is to start the computer operating system after the power is turned on. and it is stored in the ROM portion of the main memory.
Computer start up :starting the execution of initial program after
computer is turned on
Boot strap loader loads the portion of disk to main memory and control is then transferred to OS.
15

## Slide 16: Auxiliary memory(SECONDARY
The most common auxilliary device used in the computer system is magnetic disk and magnetic tape.
Store large amount of data permanantly.
Portable
Types of auxilliary memory
Magnetic disk
Magnetic tape
MEMORY)
16

## Slide 17: Magnetic disk
circular plate ,made of metal or plastic coated with magnetize material. High speed of rotation
Bits are store in a concentric circle called tracks.
Division of tracks are called sectors.
17

## Slide 18: Magnetic disk
18

## Slide 19: Magnetic tape
Sequential access memory used for storing,backup,audio,video data etc .
Highly reliable memory.
Slower for read write operation.
19

## Slide 20: Magnetic tape
20

## Slide 21
RAM AND ROM CHIP
21

## Slide 22: RAM AND ROM CHIPS
22
RAM chip:
Used for communication with the CPU if one or more control inputs.
requires 7-bit address and an 8-bit bidirectional data bus.
 chip select (CS) are for enabling the chip.

## Slide 23
Fig. RAM chip
23

## Slide 24:  when CS1=1 and (CS2)’=0, the unit in operation.
High impedance state indicates open circuit.
When CS1=1 and (CS2)’=0, the memory is places in a R/W mode.
When the RD input is enabled, the content of the selected byte is placed into the
data bus.
24

## Slide 25: ROM chip
25

## Slide 26: A ROM chip is unidirectional.
26
9 address lines to address 512 bytes.
 chip select CS1=1 and (CS2)’=0 for the unit to operate.
Otherwise, the data bus in a high-impedance state.

## Slide 27: VIRTUAL MEMORY
27

## Slide 28: Attempts to optimize the use of the main memory(the high
speed portion) with the hard disk (the lower speed portion).
Technique for using the secondary storage to extend the apparent limited size of the physical memory beyond its physical size .
 Implemented since the available physical memory will not be enough to host all the program.
28

## Slide 29: Address space and Memory space
An address used by the programmer is virtual memory , the set of such address is called address space.
An address in main memory is location ,the set of such location is called memory space.
Example: consider main memory :32k words(k=1024)=2^15 and auxiliary memory 1024k words=2^20(to address 15 bits of physical memory and 20 bits of virtual memory is required)
29

## Slide 30
.
30

## Slide 31
.
31
In our example we have 20-bit address of an instruction (to refer 20-bit virtual address) but physical memory addresses are specified with 15-bits. So a table is needed
to map a virtual address of 20-bits to a physical address of 15-bits.
Mapping is a dynamic operation, which means that every address is translated immediately as a word is referenced by CPU.

## Slide 32
32

## Slide 33: Address Mapping using Pages
Blocks (or page frame): Blocks are the groups of equal size which are broken down from physical memory and ranges from 64 to 4096words each.
Pages: refers to a portion of subdivided virtual memory having same size as blocks i.e. groups of address space.
33

## Slide 34: Example: consider computer with address space = 8K and memory space = 4K.
If we spit both spaces into groups of 1k words we get 8 pages and 4 blocks.
blocks.
34

## Slide 35
Page Replacement
A virtual memory system is a combination of hardware and software techniques. A memory management software system handles:
Which page in main memory should be removed to make room for a new page?
 When a new page is to be transferred from auxiliary memory to main memory?
35

## Slide 36
36
 Where the page is to be placed in main memory?
There are numerous page replacement algorithms, two of which are:
First-in First-out (FIFO): replaces a page that has been in memory longest time.
Least Recently Used (LRU): assumes that least recently used page is the better candidate for
removal than the least recently loaded page.

## Slide 37
37 When a page fault occurs in a virtual memory system, it signifies that the page referenced by the program is not in main memory. A new page is then transferred from auxiliary memory to main memory. If main memory is full, it would be necessary to remove a page from a memory block to make a room for a new page. The policy for choosing pages to remove is determined from the replacement algorithm that is used.
GOAL: try to remove the page least likely to be referenced by in the immediate future.

## Slide 38: Memory Management Hardware
38

## Slide 39
Introduction
Collection of hardware and software procedures for managing various program.
39

## Slide 40: Basic component of MMU
Sharing common program by multiple user
Protection of information unauthorized
40

## Slide 41: Segmented Page Mapping
Length of each segment allowed to grow and contract according need of program execution.
Way of specifying the length of a segment by associating with it a no. of equal sized page
Consider diagram below
41

## Slide 42
42

## Slide 43: In above fig:
Consider
Logical Address=Segment+page+word segment specifies segment no.
Page field specifies page within the segment
Word field specifies specific word within the page
43

## Slide 44
44

## Slide 45
45