## Slide 1: Topic: Pipelining

## Slide 2
A Pipelining is a series of stages, where some work is done at each stage in parallel.
The stages are connected one to the next to form a pipe - instructions enter at one end, progress through the stages, and exit at the other end.

## Slide 3: Pipelining Case: Laundry
4 loads of laundry that need to washed, dried, and folded.
  30 minutes to wash, 40 min. to dry, and 20 min. to fold.
  We have 1 washer, 1 dryer, and 1 folding station.
What’s the most efficient way to get the 4 loads of laundry done?

## Slide 4: Non Pipelined Laundry
Takes a total of 6 hours; nothing is done in parallel

## Slide 5: Pipelined Laundry
Using this method, the laundry would be done at 9:30.

## Slide 6: Definition: Pipelining is an speed up technique where multiple instructions are overlapped in execution on a processor.

## Slide 7: Pipelining: Processors
Computers, like laundry, typically perform the exact same
steps for every instruction:
  Fetch an instruction from memory
  Decode the instruction
  Execute the instruction
  Read memory to get input
  Write the result back to memory

## Slide 8: Instruction Pipeline
CS211 8
Instruction execution process lends itself naturally to pipelining
– overlap the subtasks of instruction fetch, decode and execute
Instruction pipeline has six operations,
  Fetch instruction (FI)
  Decode instruction (DI)
  Calculate operands (CO)
  Fetch operands (FO)
  Execute instructions (EI)
  Write result (WR)
Overlap these operations

## Slide 9: Instructions Fetch
CS211 9
The IF stage is responsible for obtaining the requested instruction from memory. The instruction and the program counter are stored in the register as temporary storage.

## Slide 10: Decode Instruction
CS211 10
The DI stage is responsible for decoding the instruction and sending out the various control lines to the other parts of the processor.

## Slide 11: Calculate Operands
CS211 11
The CO stage is where any calculations are performed. The main component in this stage is the ALU. The ALU is made up of arithmetic, logic and capabilities.

## Slide 12: Fetch Operands and Execute Instruction
CS211 12
The FO and EI stages are responsible for storing and loading values to and from memory. They also responsible for input and output from the processor respectively.

## Slide 13: Write Operands
CS211 13
The WO stage is responsible for writing the result of a calculation, memory access or input into the register file.

## Slide 14: Six Stage Instruction Pipeline

## Slide 15: Timing Diagram for Instruction Pipeline Operation

## Slide 16: Pipeline Performance: Clock & Timing
CS211 16
Si
Si+1

m
d
Clock cycle of the pipeline : 
Latch delay : d
 = max {m } + d
Pipeline frequency : f
f = 1 / 
6

## Slide 17: Pipeline Performance: Speedup & Efficiency
CS211 17
k-stage pipeline processes n tasks in k + (n-1) clock cycles:
k cycles for the first task and n-1 cycles for the remaining n-1 tasks
Total time to process n tasks
Tk = [ k + (n-1)] 
For the non-pipelined processor
T1 = n k 
Speedup factor
k
S =
T1
T
k
=
n k  [ k + (n-1)] 
=
n k
k + (n-1)
7

## Slide 18: Advantages
Pipelining makes efficient use of resources.
Quicker time of execution of large number of instructions
The parallelism is invisible to the programmer.

## Slide 19: Can Pipelining Get Us Into Trouble?
CSE431 L06 Basic MIPS Pipelining.19 Irwin, PSU, 2005
Yes: Pipeline Hazards
  structural hazards: attempt to use the same resource by two different instructions at the same time
  data hazards: attempt to use data before it is ready
    An instruction’s source operand(s) are produced by a prior
instruction still in the pipeline
  control hazards: attempt to make a decision about program control flow before the condition has been evaluated and the new PC target address calculated
    branch instructions
Can always resolve hazards by waiting
  pipeline control must detect the hazard
  and take action to resolve hazards