## Slide 1: Automatic Transmission

## Slide 2: Automatic Transmission
An automatic transmission, also called auto, self-shifting transmission.
It is a type of transmission that can automatically change gear ratios as the vehicle moves, freeing the driver from having to shift gears manually.

## Slide 3: Devices Used in Automatic Transmission
Torque converter
Epicyclic gear box
Transmission Oil Pump
Clutch packs & Brake bands
Freewheel or Overrunning clutch
Hydraulic service and Control valves
Manual or Electronic Operated Shift Control

## Slide 4: Epicyclic gear train
Gear Ratio = T(Driven)/T(Driver)
Ring Gear Stationary
Sun Gear : Driver
Planet Gear : Driven
Sun Gear Stationary
Ring Gear : Driver
Planet Gear : Driven

## Slide 5: Epicyclic gear train
Ring Gear Stationary
Planet Driver & Sun Driven
  GR = 30/120 = 0.25:1
Sun Driver & Planet Driven
  GR = 120/30 = 4:1
Planet Gear Stationary
Sun Driver & Ring Driven
  GR = 90/30 = 3:1
  (Opposite Rotation)
Ring Driver & Sun Driven
  GR = 30/90 = 0.66:1
Sun Gear : 30
Ring Gear : 90
Planet : 120

## Slide 6: Automatic Transmission

## Slide 7: Automatic Transmission
2 Input &1 Output
  Input 1 = Ring Gear
  Input 2 = Sun Gear
  Output = Planet
Ring Gear Stationary (Input 1= 0)
  Rotation is given to Input 2 (Sun Gear)
  Rotation is obtained at Output (Planet Gear)
Ring Gear starts rotate (Input 1= Increases)
  Output Speed Increases
Input 1 = Input 2 (Planet does not Spin)
  Input Speed = Output Speed
Ring Gear Speed increases further
  Input 1 > Input 2
  Output Increases

## Slide 8
1st Gear : A3 is Locked with B3 cause C2 & A1 stationary (Large gear reduction takes place)
2nd Gear : A2 is locked with B2 (less gear reduction takes place)
3rd Gear : S1 held stationary by brake B1
Direct (Top) Gear : S1 locked to input shaft by applying clutch.
Reverse Gear : A4 is locked with B4.
Wilson Gear Box

## Slide 9: Torque Converter

## Slide 10: Torque Converter
Turbine blade angle is such that it changes the direction of oil flow (Reverse direction).
If this reverse direction is not changed
  Oil leaving the turbine will enters in opposite direction of pump rotation & slow down its speed.
Reverse direction changed by Stator
  Oil returns from turbine to pump in favorable direction (same in which pump is rotating).
Again pump throw the oil back to turbine & this goes continuous.
Repeated pushing of turbine blade cause the torque on turbine to increase, its called torque multiplication. (torque multiplication = 2.1 to 2.6)
  If turbine is stationary & pump rotating fast than maximum torque multiplication occurs, its called Stall.

## Slide 12: Torque Converter
When vehicle moves turbine speed increases & torque multiplication decreases.
Torque multiplication becomes unity when turbine speed = pump speed. (direct drive)
When turbine speed = 80 to 90% of pump speed
  Oil leaves turbine in forward direction & hitting back of stator blade.
  This delay the smooth flow of oil from turbine to pump.
This unwanted situation can be avoid by mounting stator on freewheel.
Freewheel allows stator to rotate in the direction of turbine & impeller. Also restrict the rotation in opposite direction.

## Slide 13: Freewheel (Overrunning Clutch)

## Slide 14: Overdrive

## Slide 15: Continuous Variable Transmission