## Slide 1
AUTOMOBILE SYSTEM

## Slide 2
Chassis
Introduction

## Slide 3
What is an ‘Automobile’??
• A vehicle producing power within itself for its propulsion is known as a Self propelled vehicle.
• Eg. Moped, Scooter, motorcycle, Car, jeep, truck, tractor, ships, aircrafts, rocket etc.
• A self propelled vehicle used for transportation of goods & passengers on the ground is called an Automobile.
• Different from Aeronautical vehicles (planes, helicopters, rockets) & marine vehicles (ships, boats, submarines)

## Slide 4
Definition of Automobile
• Automobile
is
a
“Self
Propelled
vehicle”
generally
driven
by
IC
Engine
and
it
is
used
for transportation of
passengers
Crouse.
• Examples :
& goods on ground – W. H.
Car, Bus, Truck, Scooter etc.

## Slide 5
History of Automobiles
Captain Nicholas Joseph Cugnot – French Army – built the first self propelled vehicle in 1768-70

## Slide 6
First Automobile
Cugnot Steam Trolley, Steam Engine powered, 1768

## Slide 7
Karl Benz
Inventor of the first gasoline powered automobile, 1886

## Slide 8
History
Invention of Wheel is major milestone in human history after fire

## Slide 9
Horse
Carts

## Slide 10
History
– 1869 Captain Nicholas
Cugnot
(French) build first Automobile
2.5mph (4.02 Kmph) in
15 minutes – 3 Wheeler
Steam
Piston's
1769 Cugnot Steamer in
HD.mp4
Front Wheel
Rear Wheel / Axle
Steam
Generator
Steering

## Slide 11
e
is
e
1801 – Richard
Carriage
threvithrick – Firs Steam
TREVITHICK'S PUFFING DEVIL
ON TREVITHICK DAY 2017.mp4
Trevithick was born in 1771
in a
mining
England.
village
He
in
was
Cornwall,
terrible
a
student–his
teachers
thought
he
was
a
“disobedient,
slow,
obstinate, [and] spoiled
boy” who
anything,
basically
would
never amount
to
and
in
fact
he was
illiterat
to tinker
h
entir
life–but he loved
with tools and machines6.
Puffing DEVIL
Wheels
Steam
Generator
Chimney

## Slide 12
1885 – Benz
Motors in Germany developed
first
Vehicle
propelled
with
IC
Engine
7
videoplayback.mp4

## Slide 13
…Contd
• 1897 – Mr. Foster from Crompton greaves,
borrowed first motor car in india
• 1901 -
INDIAN
Mr. Jamshed Ji TATA was the first
to
own
a
motor
car
.
Sir Jamshed Ji TATA

## Slide 14
Classification
• Purpose
• Passenger Carriers – Car, Bus
• Goods Carriers - Trucks
• Fuel Used
• Petrol
• Diesel Gas
• Electric
• Steam – not in use
• Capacity
• HMV – Trucks, Buses
• LMV – Tempo, Jeeps
of
Automobiles
•
Construction
• Single unit
• Articulated – Eg. Trailers, Tractors
Drive
• Left hand
• Right Hand
Number of Wheels
• Two Wheeler
• Three Wheeler
• Four Wheeler
Body
• hatchback
• Sedan
• Convertibles
• Station Wagons - Vans
•
•
•
• Special Purpose Vehicles

## Slide 16
Engine
SI – Spark Ignition
CI – Compression
Two Stroke
Ignition
Four
Stroke

## Slide 17
Chassis & Other
important Parts
Vehicle BODY

## Slide 18
UNIT-I
Chassis

## Slide 19
Chassis
Main Supporting Structure of vehicle consist of almost all major parts except automobile body

## Slide 20
Key component of Chassis
Frame Have 3 different types
is
Frame
1.
2.
3.
Conventional frame
Integral Frame
Semi Integral Frame
Functions of Frame
• To support chassis components & body
• Withstand the static & dynamic load of different components of chassis
• To withstand load of the body
• To carry load
• To withstand stresses caused due to uneven road conditions.
• To withstand force caused due to turning of the vehicles &
sudden braking or acceleration.

## Slide 21
15
REAR
FRONT

## Slide 23
17

## Slide 24
Frame
Cross
Sections
Channel Section – Good Resistance
to Bending
Box Section – Good Resistance to both bending
and torsion
Tubular Section – Good Resistance to torsion.

## Slide 25
Types
of Chassis
• According to layout
• Conventional
• Forward
• Semi forward
• According to mounting of engine and transmission
• Engine at front
• Engine fitted in front but crosswise
• Engine fitted at the center of the chassis
• Engine fitted at the back

## Slide 26
According
to
mounting
of
Component
of
Chassis
• Front Engine Rear Wheel Drive
• Front Engine Front Wheel Drive
• Rear Engine Rear Wheel Drive
• All Wheel Drive

## Slide 27
Conventional Chassis
Affects visibility of driver
Engine is fitted in front of the driver cabin or driver seat such as in cars.
Chassis portion can not be utilized for carrying passengers and goods
Heavy Engine can be fitted, which can used to give more power

## Slide 28
Semi
Forward
Chassis
• Half portion of the engine is in the driver cabin
half is outside the cabin such as in Tata trucks /
& and remaining
Tempos
• In this arrangement a part of the chassis is utilized for carrying
extra passengers

## Slide 29
Forward
Chassis
• Complete engine is mounted inside the driver cabin, Driver seat
is just above the front wheel.
• More Boot Space Available as full utilization of chassis

## Slide 30
Engine
Conventionally
at
front
•
the
engines
are
fitted
at front
&
drive
is
given to
“rear”
the
wheels
from the
•
•
Advantages
Enough space is available for luggage behind the rear seat
The weight of vehicles is well
balance
•
•
Increased
efficiency
of
cooling system
24

## Slide 31
Engine fitted in front but crosswise
•
This
front
engine
layout
requires very small space to
fit the engine. Hence, most
compact cars use this layout
which has very small space to
accommodate the engine.
Design is more complicated
•
as
compared
to
the
longitudinally placed engine.
This is because it does not
leave
enough
space
for
accessories.

## Slide 32
Engine
is
mounted
at
center
•
Mid-engine,
rear-wheel drive
format can
be considered the
original layout of automobiles.
Drive is given to the rear.
Equal Distribution of weight.
•
•
•
Largest drawback of mid-engine
cars is
space;
restricted rear passenger
•
Consequently most mid-engine
vehicles are two-seat vehicles.
The engine in effect pushes the
passenger compartment forward
towards the front axle (if engine is
behind driver).
•

## Slide 33
Engine
Fitted
at
back
•
Flat floor is available since
long
propeller
shafts
are
eliminated
•
With
propeller
elimination
of
center
giving
shaft
the
of
gravity
lowered
stable driving
Better adhesion
•
on road
climbing
specially
hill
when

## Slide 34
Other
important
chassis
types
• Tabular Space Frame
• Monocoque Frame
• Backbone Frame
28

## Slide 35
r
r
h
• Fo
highe
y
stre
Tubular
Frame
•
•
It is 3-dimensional design
Tubular space frame chassis employs dozens of circular section tube, positions in
different
directions
to
provide mechanical strength against force from anywhere.
•
These tubes are welded &
forms
a
very
complex
structure.
ngt
required
b
sports
cars, tubular space
frame
chassis
usually
incorporate a strong structure under both doors.

## Slide 36
Advantages
&
Dis
advantages
• Very
strong
in
any •
Very complex , costly
and time consuming to
be built.
It engages a lot of
spaces rise the door seal
and result in difficult to
access to the cabin.
direction
with ladder
Monocoque
(compared
chassis and
chassis
of
•
the
same
weight)
•
Impossible
for
robotized production.

## Slide 37
Monocoque
Monocoque is a one-piece structure which defines overall shape of the car. while ladder, tabular & backbone provide only stress members.
Today 99% car produced in this planet are made of steel Monocoque chassis.
Chassis are made by welding of Several pieces. (Spot Welding )
Monocoque is made of steel
31

## Slide 38
Advantages
&
Disadvantages
• Space-efficiency.
• Monocoque
•
chassis •
It is very heavy.
Impossible for small
volume production.
In case of accidents
benefit crash production
because it uses
metal.
a
lot of
•
whole structure
obsolete.
become
• Cheap
production
for
mass

## Slide 39
Back
• Similar
design.
Bone
Frame
to the body frame
• It consist
backbone
of a strong tubular
(Usually
rectangular in C/s).
• A body is placed on the structure.
• This type of chassis has been
used in numerous sports cars.

## Slide 40
licated an
.
d m
,
ore
e
costly
How
eve
r
ll
th m
-
ore
axles
with
wheel
drive
are ne
eded,
t
he co
st
benefit tur
ns in f
e
sis
Advantages
&
Disadvantages
•
The vulnerable parts of the
drive shaft are covered by a
•
Manufacturing
backbone chassis
comp
the
more
is
thick
tube.
The
whole
system is extremely reliable.
However,
if
a
problem
occurs, repairs are more
complicated.
avor
of
backbon chas
.
•
The modular system enables
configurations of 2-, 3-, 4-,
5-, 6-, or 8-axle vehicles
•
The backbone
chassis
is
heavier for a given torsional
stiffness than a uni-body.
with various wheel
bases.
The
chassis
gives
no
side
protection
impacts.
against
34

## Slide 41
Types
of
Vehicle
Layout
Or
Chassis
Layout
35

## Slide 42
Front
Engine
Rear
Wheel
Drive
Engine
Transmission
Drive Shaft
Clutch
Final Drive

## Slide 43
Front
Drive
Engine
Rear
Wheel
• Most common type of layout.
• Engine Located at front and driving power is given
to rear wheels.
• Driving Power
flows from engine to rear wheel
through
various
mechanical
linkages.

## Slide 44
ation, making the rear
ltaneous acceleration es.
Advantages
&
Disadvantages
• Better handling : - Accelerating force is applied to
the rear wheels, on which the down
due to load transfer in acceler
force
increases,
tires better able to take simu
and
curving
than
the
front
tir
ON DRY ROAD ONLY

## Slide 45
Even
weight
distribution
• The division of weight between the front and rear
wheels has a significant impact on a
car's handling,
and
it
is
much
easier
to
get
a
50/50
weight
distribution in a rear wheel drive car.
Steering radius
• As no complicated drive shaft joints
are required at
the front wheels, it is possible to turn them further
than
would
be
possible
using
front
wheel
drive,
resulting in a smaller steering radius.

## Slide 46
Less
load
at front
axle
• The driving force is given at rear axle hence there is
no
need
to
provide
complex
design
on
front
axle.
Effective Cooling of the engine due
to
exposure of cooling system to flowing air

## Slide 47
Disadvantages
Decreased interior space – This isn't an issue in a vehicle with a ladder frame like a pickup truck, where the space used by the drive line is unusable for passengers or cargo. But in a passenger car, rear wheel drive means: Less front leg room (the transmission tunnel takes up a lot of space between the driver and front passenger), less leg room for center rear passengers (due to the tunnel needed for the drive shaft), and sometimes less trunk space (since there is also more hardware that must be placed underneath the trunk).

## Slide 48
Less
Inner
space

## Slide 49
Increased
weight
• The drive shaft, which connects the engine at the
front to the drive axle in the back, adds weight.
There is extra sheet metal to form the transmission
tunnel. A rear wheel drive car will weigh
slightly
more than a comparable front
wheel
drive
car,
but
less
than
four
wheel
drive.

## Slide 50
Higher
purchase
price
• Due to the added cost of materials, rear wheel
drive
is
typically
slightly
more
expensive
to
purchase
vehicle.
.
than
a
comparable
front
wheel
drive

## Slide 51
Front
Engine
Front
Wheel
Drive
Engine
Transmission
Final Drive

## Slide 52
Front
Drive
Engine
Front
Wheel
•
In this type the engine is
mounted on the front side
of
the vehicle and
the
driving power is given to
the front wheels only.
The power flows from
engine to front axle.
This type of arrangement
•
•
have
additional
sub
type
cross
i.e.
front
mounted
engine.

## Slide 53
Advantages
• Interior space:
• Since the powertrain
engine compartment
is a single unit contained in the
of the vehicle, there is no need
to
devote
interior
space
for
a driveshaft
tunnel
or
for
rear differential, increasing
the volume
available
passengers
and
cargo.
Inner
SPACE
Engine

## Slide 54
Better
handling
on
slippery
surface
• Slippery-surface traction: placing the mass of the
drivetrain
over
the
driven
wheels
improves traction on wet, snowy, or icy surfaces.
Improved
drive
train
efficiency
• The
direct
connection
between
engine
and
transaxle reduce the mass and
of the drivetrain compared to
mechanical inertia
a rear-wheel drive
vehicle
with
a
similar
engine
and
transmission,
allowing greater fuel economy.

## Slide 55
Disadvantages
• Less Turning Radius
• The drive shafts may limit the amount by which the
front wheels can turn, they are generally unable to
make the.
• More Weight on front results in rapid wear of
front tires.
• Front-wheel drive has worse acceleration than rear-wheel drive, which is why most sporty and race cars use rear-wheel drive.

## Slide 56
Steering
AWD
FWD
VS
RWD
VS

## Slide 57
FWD
VS
RWD

## Slide 58
Rear
Engine
Rear
Wheel
Drive

## Slide 59
54

## Slide 60
Advantages
• Weight over rear wheels, increased traction while
accelerating.
• Front axle construction is simplified.
• Absence of propeller shaft results in decrease of floor height.
• Engine components mounted at rear of rear axle
hence more space is available.

## Slide 61
Disadvantages
• Separate cooling mechanism
is needed for
effective cooling
mounted at rear.
of
the
engine
as the
engine
is
• More load on rear side may result in overturning
(Over steer) of the vehicle.
• Longer linkages are required to operate clutch,
gears from driver.

## Slide 62
All
wheel
Drive

## Slide 63
AWD
or
4WD
All wheels Always
engaged.
Safe and advantageous over 4WD
4 wheels can be engaged only in difficult terrain.
In normal condition power is given to rear wheels only.

## Slide 64
Advantages
• 4WD improves traction
in dangerous driving
conditions,
such
as
snow,
make
ice,
rocks,
and
other
scenarios that can
control
difficult.
By
engaging both sets of wheels, traction and control
improves.
• Additional weight contributes to better grip on the
road.
• 4WD is great for those who like off-roading.

## Slide 65
Disadvantages
•
The main disadvantage of 4WD is added cost for
purchase, maintenance, and fuel. The extra equipment
(differentials, transfer case, etc.) adds complexity and
weight to the vehicle, increasing initial market value,
tire wear, and the cost of repairs and maintenance.
The added power and weight of 4WD and AWD systems require more fuel, making them less efficient than their 2WD counterparts.
Added weight improves traction and control, but it also increases the braking distance required to make a complete stop. Lighter vehicles can avoid collision easier than heavier vehicles.
•
•