## Slide 1: Digital Electronics Components
Miloni Ganatra

## Slide 2: Logic Gates
Fundamental building block of digital System.
To Make decisions
It produces one output level when combination of input levels are present & different output level when other combination of input levels are present.
O/P is dependent only state of the input at that instant
Three basic gates –AND ,OR ,NOT

## Slide 3
5v
The NOT gate is the first of the three fundamental logic gates.
The NOT Gate (inverter):
Input A
Output X
A | X
0 | 1
1 | 0
Truth Table: Is a chart that lists the input condition on the left and the gate’s output response on the right. The table shows that the NOT gate responds at the output with the inverse of the signal applied to the input.
Slide #
Logic 1
OFF
Logic 0
ON
Logic 1
OFF
Logic 0
ON
Logic 1
OFF
Logic 0
ON

## Slide 4
The AND Gate:
Truth Table: The table shows that the AND gate responds with a high at the output if the signal applied to the input A and B are both high.
5v
5v
5v
Input A
Output X
Input B
AND
Slide #
Logic 0
Logic 0
Logic 0
Logic 0
Logic 0
Logic 1
Logic 1
Logic 0
Logic 0
Logic 1
Logic 1
Logic 1
A | B | X
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

## Slide 5
The OR Gate:
Truth Table: The table shows that the OR gate responds with a high at the output if the signal applied to the input A or B is high.
Input A
Output X
Input B
OR
5v
5v
5v
Slide #
Logic 0
Logic 0
Logic 0
Logic 0
Logic 1
Logic 1
Logic 1
Logic 1
Logic 0
Logic 1
Logic 1
Logic 1
A | B | X
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 6
5v
5v
5v
Logic 1
Logic 1
Logic 0
Logic 0
Logic 1
Logic 1
Logic 1
Logic 0
Logic 1
NAND Gate
The NAND gate is equivalent to an AND gate with a NOT gate connected to its output. NAND comes from the words Not AND
Input A
Output X
Input B
NAND
Logic 0
Logic 1
Logic 0
Boolean Equation: here is the equation for the NAND gate.
A | B | X
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
NAND Symbol
Slide #

## Slide 7
Logic 1
Logic 0
Logic 0
Logic 0
Logic 0
Logic 1
Logic 1
Logic 0
Logic 1
NOR Gate
The NOR gate is equivalent to an OR gate with a NOT gate connected to its output. NOR comes from the words Not OR.
Input A
Output X
Input B
NOR
5v
5v
5v
Logic 0
Logic 1
Logic 0
Boolean Equation: here is the equation for the NOR gate.
A | B | X
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
NOR Symbol
Slide #

## Slide 8
XOR Gate & XNOR Gate
The XOR gate is an exclusive OR gate. It will output a logic 1 if there is an exclusive logic 1 at input A or B. Exclusive means: Only one input can be high at one time.
Input A
Output X
Input B
XOR
XOR Boolean Equation:
A | B | X
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
The XNOR gate is an exclusive OR gate with an NOT gate at the output. It will output a logic 0 if there is an exclusive logic 1 at input A or B.
A | B | X
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
Input A
Output X
Input B
XNOR
XOR Boolean Equation: